## Slide 1
Lecture 5: Parallel Architecture
Lecturer:
Simon Winberg
Digital Systems
EEE4084F
Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)

## Slide 2
Quiz on Thursday!
2pm
Lectures 1-4
Seminar 1

## Slide 3: Lecture Overview
Processor Architecture types
  Von Neumann; Flynn’s taxonomy
Class activity
Memory access architectures

## Slide 4: Types of Processor Architecture
EEE4084F

## Slide 5: von Neumann Architecture
Named after John von Neumann
  A Hungarian mathematician. He was the first to write about requirements for an electronic computer (done in 1945).
The ‘von Neumann computer’ differed from earlier computers that were programmed by hard wiring.
Most computers since then have followed this design

## Slide 6: von Neumann Architecture
The von Neumann computer comprises the following four components:
  Memory
  Control Unit
  Arithmetic Logic Unit (ALU)
  Input/Output
Figure 1: The Von Neumann architecture*
(* image adapted from http://en.wikipedia.org/w/index.php?title=Von_Neumann_architecture)
See 1-page reading in Resources on VULA

## Slide 7: von Neumann Architecture: Memory
Random access, read/write memory stores both programs and data
Program comprises instructions (von Neumann termed ‘machine instructions’) that tells the computer what do.
Data is simply information to be used by the program

## Slide 8: von Neumann Architecture: Operation
Control unit fetches instruction or data from memory, decodes and executes the instruction, sequentially completes sub-operations for the instruction
Arithmetic Unit performs basic arithmetic operations (earlier CPUs didn’t have multiply or divide; had few instructions, e.g. LOAD, STORE, ADD, IN, OUT and JUMP on flags)
Input/Output is interface to other systems and human operator

## Slide 9: Suggested further learning
Simple recap of Von Neumann Arch:
  http://www.youtube.com/watch?v=DMiEgKZ-qCw
Some history of Von Neumann leading towards his machine: (not examined!)
  “The Greatest Computer Programmer Was Its First”
  http://www.youtube.com/watch?v=Po3vwMq_2xA

## Slide 10: Flynn’s taxonomy
Flynn’s (1966) taxonomy was developed as a means to classify parallel computer architectures
Computer system can be fit into one of the following four forms:
SISD
Single Instruction Single Data
SIMD
Single Instruction Multiple Data
MISD
Multiple Instructions Single Data
MIMD
Multiple Instructions Multiple Data
Not to be confused with the terms of “Single Program Multiple Data (SPMD)” and “Multiple Program Multiple Data (MPMD)”.
Flynn’s
Taxon.
MI
MD

## Slide 11: Single Instruction Single Data (SISD)
This is (obviously) the classic von Neumann Computer: serial (not parallel) computer, e.g.:
  Old style single core PC CPUs, e.g. i486
Single instruction 
  One instruction stream acted on by the CPU during any one clock cycle
Single data 
  Only one input data stream for any one clock cycle
Deterministic execution
0x1000
LD A,[0x2002]
0x1003
LD B,[0x2004]
0x1006
ADD A,B
0x1007
SHL A,1
0x1008
ST A,[0x2000]
x = 2 * (y + z);

## Slide 12: Single Instruction Multiple Data (SIMD)
A form of parallel computer
  Early supercomputers used this model first
  Nowadays it has become common – e.g., used in modern computers on GPUs
Single instruction 
  All processing units execute the same instruction for any given clock cycle
Multiple data 
  Each processing unit can operate on a different data element
LD AX,[DX+0]
LD BX,[EX+0]
ADD AX,BX
SHL AX,1
ST AX,[CX+0]
y= [1 2 3 4]
z = [2 3 4 5]
x = 2 * (y + z)
…
LD AX,[DX+3]
LD BX,[EX+3]
ADD AX,BX
SHL AX,1
ST AX,[CX+3]
…
…
CPU 1
CPU 4

## Slide 13: Single Instruction Multiple Data (SIMD)
Runs in lockstep (i.e., all elements synchronized)
Works well for algorithms with a lot of regularity; e.g. graphics processing.
Two main types:
  Processor arrays
  Vector pipelines
Still highly deterministic (know the same operation is applied to specific set of data – but more data to keep track of per instruction)

## Slide 14: Single Instruction Multiple Data (SIMD) Examples
Vector pipelines
  IBM 9000, Cray X-MP, Fujitsu vector processor, NEC SX-2, Hitachi S820, ETA10
Processor arrays
  Thinking Machine CM2, MasPar MP-1 & MP-2, ILLIAC IV
Graphics processor units usually use SIMD
Cray X-MP
MasPar MP-1

## Slide 15: Multiple Instruction Single Data (MISD)
Single data stream fed into multiple processing units
Each processing unit works on data independently via independent instruction streams
Few actual examples of this class of parallel computer have ever existed

## Slide 16: Multiple Instruction Single Data (MISD) Example
…
…
…
Possible uses? Somewhat intellectual?
  Maybe redundant! (see next slide)
Possible example application:
  Different set of signal processing operations working the same signal stream
x = +MAXINT
Example:
Simultaneously find the min and max input, and do a sum of inputs.
x = -MAXINT
x = 0
If A<x then x = A
If A>x then x = A
x = x + A
A = input
CPU 1
CPU 2
CPU 3

## Slide 17: Multiple Instruction Multiple Data (MIMD)
The most common type of parallel computer (most late model computers, e.g. Intel Core Duo, in this category)
Multiple Instruction 
  Each processor can be executing a different instruction stream
Multiple Data 
  Every processor may be working with a different data stream
Execution can be asynchronous or synchronous; non-deterministic or deterministic

## Slide 18: Multiple Instruction Multiple Data (MIMD)
Examples
  Many of the current supercomputers
  Networked parallel computer clusters
  SMP computers
  multi-core PCs
MIMD architectures could include all the other models. e.g.,
  SISD – just one CPU active, others running NOP
  SIMD – all CPUs load the same instruction but apply to different data
  MISD – all CPUs load different instructions but apply it to the same data
AMD Opteron
IBM BlueGene

## Slide 19: Class Activity
Consider the types of programming models:
Sequential / non-parallel
Data parallel model
Message passing model
Shared memory model
Hybrid models
Types of architecture models
SISD
Single Instruction Single Data
SIMD
Single Instruction Multiple Data
MISD
Multiple Instructions Single Data
MIMD
Multiple Instructions Multiple Data
Consider an application:
Transaction processing
Face recognition
3D graphics rendering
Pattern search (or string search)
Radar
Database queries
Step 1: choose an application
Step 2: which programming model would you like to use?
Step 3: which computer architecture would you use?
TODO: Work in groups. Follow steps 1-3 shown for a selection of the applications listed in step 1.
We will them vote on the choices.
Your task
(1)
(2)
(3)
(4)

## Slide 20: Voting for Flynn’s
SISD
Single Instruction Single Data
SIMD
Single Instruction Multiple Data
MISD
Multiple Instructions Single Data
MIMD
Multiple Instructions Multiple Data
(1)
(2)
(3)
(4)
Program | SISD(1) | SIMD(2) | MISD(3) | MIMD(4)
Transaction processing |  |  |  | 
Face recognition |  |  |  | 
3D graphics rendering |  |  |  | 
Pattern search |  |  |  | 
Radar |  |  |  | 
Database queries |  |  |  | 
SQ = Sequential / non-parallel
DP = Data parallel model
MP = Message passing model
SM = Shared memory model
HM = Hybrid models
SQ
MH: SM+MP
SM
DP
MP
(MP)
DP
Click to see my suggested answers…
Many of these are somewhat debatable. In a quiz situation it would probably be a good idea to add comments to your answer motivating your choices.

## Slide 21: Thursday planning
2pm : Quiz
3pm : Presentation and discussion of Conceptual Assignment (mini project 1)

## Slide 22: Memory Access Architectures
EEE4084F
The remaining slides should be considered a reading assignment. Much of this information mirrors the programming models presented in Lecture 4. The slides that follows are examinable in quizzes/exams.
Reading assignment

## Slide 23: Parallel computer memory architectures
The choice of memory architecture is not necessarily dependent on the ‘Flynn classification’
For a SISM computer, this aspect is largely irrelevant (but consider a PC with GPU and DMA as not being in the SISM category)

## Slide 24: Shared Memory Architectures
Generally, all processors have access to all memory in a global address space.
Processors operate independently, but they can share the same global memory.
Changes to global memory done by one processor are seen by the other processors.
Shared memory machines can be divided into two types, depending on when memory is accessed:
  Uniform Memory Access (UMA) or
  Non-uniform Memory Access (NUMA)

## Slide 25: Uniform Memory Access (UMA)
Common today in form of Symmetric Multi-Processor (SMP) machines
  Identical processors
  Equal access and access times to memory
  Cache coherent
Cache coherent =
    When one processor writes a location in shared memory, all other processors are updated.
    Cache coherency is implemented at the hardware level.
MEMORY
CPU
CPU
CPU
CPU

## Slide 26: Non-Uniform Memory Access (NUMA)
Not all processors have the same access time to all the memories
Memory access across link is slower
If cache coherency is maintained, then may also be called CC-NUMA - Cache Coherent NUMA
CPU
MEMORY
CPU
CPU
MEMORY
CPU
Interconnect bus
SMP 1
SMP 2
This architecture has two SMPs
connected via a bus. When a CPU on SMP1 needs to access memory connected to SMP2, there will be some form of lag which may be a few times slower than access to SMP1’s own memory.

## Slide 27: Shared memory pros & cons
Advantages
  Global address space gives a user-friendly programming approach (as discussed in shared memory programming model)
  Sharing data between tasks is fast and uniform due to the proximity of memory to CPUs
Disadvantages:
  Major drawback: lack of scalability between memory and CPUs.
  Adding CPUs can increases traffic on shared memory-CPU path (for cache coherent systems also increases traffic associated with cache/memory management)

## Slide 28: Shared memory pros & cons
Disadvantages
  Programmer responsible for implementing/using synchronization constructs to make sure that correct access of global memory is done.
  Becomes more difficult and expensive to design and construct shared memory machines with ever increasing numbers of processors.

## Slide 29: Distributed memory
Similar to shared memory, but requires a communications network to share memory
Local Memory
CPU
Communications network
Local Memory
CPU
Local Memory
CPU
…
Each processor has its own local memory (not directly accessible by the other processors’ memory addresses)
Processors connected via a communication network – the communication network fabric varies; could simply be Ethernet.
Cache coherency does not apply (when a CPU changes its local memory, the hardware does not notify the other processors – if needed the programmer needs to provide this functionality)
Programmer responsible for implementing methods by which one processor can access memory of a different processor.

## Slide 30: Distributed Memory: Pros & Cons
Advantages:
  Memory scalable with number of processors
  Each processor can access own memory quickly without communication overheads or maintaining cache coherency (for UMA).
  Cost benefits: use of commercial off-the-shelf (COTS) processors and networks

## Slide 31: Distributed Memory: Pros & Cons
Disadvantages:
  Programmer takes on responsibility for data consistency, synchronization and communication between processors.
  Existing (legacy) programs based on shared global memory may be difficult to port to this model.
  May be more difficult to write applications for distributed memory systems than it is for shared memory systems.
  Restricted by non-uniform memory access (NUMA) performance (meaning a memory access bottle neck that may be many times slower than shared memory systems)

## Slide 32: Distributed Shared Memory (i.e. Hybrid) System
Simply a network of shared memory systems (possibly in one computer or a cluster of separated computers)
Use in many modern supercomputer designs today
Shared memory part is usually UMA (cache coherent)
Pros & Cons? – Best and Worst of two worlds.

## Slide 33
End of Lecture

## Slide 34
Image sources:
Title slide: California High-Speed Rail - Wikipedia (open commons)
Von Neumann photo - Wikipedia (open commons)
Computer and box clipart – open commons
Chat icon clipart - http://openclipart.org/tags/chat (public domain)
Computer photos - Wikipedia (open commons)
Book clipart drawing slide 22 onwards - Wikipedia (open commons)
Disclaimers and copyright/licensing details
I have tried to follow the correct practices concerning copyright and licensing of material, particularly image sources that have been used in this presentation. I have put much effort into trying to make this material open access so that it can be of benefit to others in their teaching and learning practice. Any mistakes or omissions with regards to these issues I will correct when notified. To the best of my understanding the material in these slides can be shared according to the Creative Commons “Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)” license, and that is why I selected that license to apply to this presentation (it’s not because I particulate want my slides referenced but more to acknowledge the sources and generosity of others who have provided free material such as the images I have used).