## Slide 1
Lecture 14
Reconfigurable Computing Basics
Lecturer:
Simon Winberg
Digital Systems
EEE4084F

## Slide 2: Lecture Overview
Reconfigurable Computing Basics
Brainstorming exercise
Introduction to Verilog

## Slide 3
Early Notice:
Quiz next
Thursday!
Quiz 2 next Tuesday (16 Apr)
Held 9am, 45 minutes
Covers:
Lecture 5 - Lecture 12
Chapters 9, 10 and 13 of the textbook (i.e. seminars 6 and 5).

## Slide 4: RC Basics
EEE4084F

## Slide 5
Why does
RC = Trendy?

## Slide 6: Why RC = Trendy
Software processors aren’t delivering:
  The speed of temporal instruction execution no long seems to be increasing
  General-purpose multi-core processors need coarse grain thread-level parallelism (tricky; may need massive rewrites of code)
Why RC is seen as a possible solution:
  FPGAs becoming able to implement more complex, integrated functions
  A means to implement spatial computation, and to perform massively-parallel computations directly in hardware

## Slide 7
Terminology moment…
Dual processing
RC application development
RC platform
RC application
RC platform development
Correlations

## Slide 8: RC application vs. platform development
RC platform development =
  Developing an infrastructure for doing RC
  E.g., developing an IBM Blade platform
RC application development =
  Using an existing RC platform
  Developing custom hardware and software for deployment on an RC platform
Focus of this course

## Slide 9: Dual Processing?
A technique to verify operation
Essentially performing the
same operation twice (if not
more times) to check for
consistency.
Often uses correlations.

## Slide 10: Dual Processing & Simulation
Used to verify computation
Run on target hardware (e.g., Nexus2)
Run on PC (C program of simulator)
Compare results
Main issue:
  Do the results match closely
  “Feel good” – at least both sides are close
When this approach is used…
  Unsure of the target hardware operation
  Investigating differences in computation

## Slide 11: Brainstorming activity
Work in groups of two or three
Discussion Point 1: What would you say is the greatest challenge that RC developers face nowadays?
Discussion Point 2: What sort of technologies or ideas do you think would assist developers and in overcoming these challenges?
Discussion Point 3: What do you think are major benefits, and major disadvantages to reconfigurable computing? Consider what kinds of application to which RC is – and is not – suited.

## Slide 12: Review of Brainstorm Activity
Greatest challenges:
  Knowing how to go from a “doorstop” to a useful and usable computer
  Conceptualizing parallelized algorithms and parallelizing sequential algorithms (e.g., the Quick Sort algorithm)
Technologies to assist developers:
  Model Integrated Computing*
  Languages designed for parallel programming
  Better knowledge management
* http://www.isis.vanderbilt.edu/research/MIC

## Slide 13: Review of Brainstorm Activity
RC suited to
  Ranges of applications that need some high-speed filtering of digital (or analogue) data which can then be fed into a processing pipe line (e.g., sample data + filter data + process + send on results).
  Course grained problems, breaking a problem into parts, working on the parts in parallel, and joining results of the parts.

## Slide 14
3G / WiMAX
relay
How SDRRG uses FPGAs + Rhino
RHINO* platform: Example and Case Study of a Reconfigurable Computing Platform and proposed Applications
Wifi Router
Radar signal
Processing
Font-end
Rhino: a platform design and built at UCT by the Software Defined Radio Research Group (SDRRG)
SDRRG focuses on using the same reconfigurable computing platform as a substantial component of the underlying RF sampling and digital processing in multiple system, and for experimental radio and reconfigurable computing related research and training.
Long-term to save substantially in prototyping costs
* RHINO = Reconfigurable Hardware Interface for computIng and radiO

## Slide 15: Rhino Architecture: A Case Study
2x 256MB DDR3 SDRAM
2x 128MB DDR2 SDRAM
2x FMC Connectors
2x CX4 (10Gbps ethernet)
256MB NAND Flash
USB, SD Card, 100Mbps Ethernet, audio and video
Software Defined Radio Research Group

## Slide 16: Conclusion & Plans for Next lecture
Next lecture:
  Programming in Verilog
  RC Architectures