## Slide 1
Lecture 6:
Architectures Types, Memory Access Architectures, Classic Microcontroller Case Studies
Digital Systems
EEE4084F
Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)

## Slide 2: Lecture Overview
Classic parallel programming techniques
Processor Architecture Types
Von Neumann; Flynn’s taxonomy
Class activity
Flynn’s Taxonomy
Memory access architectures
Case Studies of classic microprocessor/ microcontroller architectures
Additional readings

## Slide 3: Classic Parallel
EEE4084F

## Slide 4: Classic techniques for parallel programming*
Single Program Multiple Data (SPMD)
  Consider it as running the same program, on different data inputs, on different computers (possibly) at the same time
Multiple Program Multiple Data (MPMD)
  Consider this one as running the same program with different parameters settings, or recompiling the same code with different sections of code included (e.g., uisng #ifdef and #endif to do this)
Following this approach performance statistics can be gathered (without necessarily any parallel code being written) and then evaluated after the effect to deem the feasibility of implementing a parallel (e.g. actual pthreads version) of the program.
*Informally know as the lazy parallel programming model.

## Slide 5: Terms
EEE4084F

## Slide 6: Terms (reminders)
Observed speedup =
Parallel overhead:
  Amount of time to coordinate parallel tasks (excludes time doing useful work).
  Parallel overhead includes operations such as: Task/co-processor start-up time, Synchronizations, communications, parallelization libraries (e.g., OpenMP, Pthreads.so), tools, operating system, task termination and clean-up time
Wallclock time initial version
Wallclock time refined version
Wallclock time sequential (or gold)
Wallclock time parallel version
=
The parallel overhead of the lazy parallel model could clearly be extreme, considering that is would rely on manual intervention to (e.g.) partition and prepare the data before the program runs.

## Slide 7: Some terms
Embarrassingly Parallel
  Simultaneously performing many similar, independent tasks, with little to no coordination between tasks.
Massively Parallel
  Hardware that has very many processors (execution of parallel tasks). Can consider this classification of 100 000+ parallel tasks.
{ Stupidly Parallel }
  While this isn’t really an official term it typically relates to instances where a big (and possibly very complex) coding effort is put into developing a solution that in practice has negligible savings or worse is a whole lot slower (and possibly erroneous/buggy) than if it was just a simpler sequential implementation.

## Slide 8: Types of Processor Architecture
EEE4084F
Type
A
Type
B
Type
C
Type
D
Type
E
Type
F
Type
G
Type
H
Type
I
Type
J

## Slide 9: von Neumann Architecture
Named after John von Neumann
  A Hungarian mathematician. He was the first to write about requirements for an electronic computer (done in 1945).
The ‘von Neumann computer’ differed from earlier computers that were programmed by hard wiring.
Most computers since then have followed this design

## Slide 10: John von Neumann & the JvN Machine
“The Greatest Computer Programmer Was Its First!”
https://www.youtube.com/watch?v=Po3vwMq_2xA

## Slide 11: von Neumann Architecture
The von Neumann computer comprises the following four components:
  Memory
  Control Unit
  Arithmetic Logic Unit (ALU)
  Input/Output
Figure 1: The Von Neumann architecture*
(* image adapted from http://en.wikipedia.org/w/index.php?title=Von_Neumann_architecture)
See 1-page reading in Resources on VULA

## Slide 12: von Neumann Architecture: Memory
Random access, read/write memory stores both programs and data
Program comprises instructions (von Neumann termed ‘machine instructions’) that tells the computer what do.
Data is simply information to be used by the program

## Slide 13: von Neumann Architecture: Operation
Control unit fetches instruction or data from memory, decodes and executes the instruction, sequentially completes sub-operations for the instruction
Arithmetic Unit performs basic arithmetic operations (earlier CPUs didn’t have multiply or divide; had few instructions, e.g. LOAD, STORE, ADD, IN, OUT and JUMP on flags)
Input/Output is interface to other systems and human operator

## Slide 14: Suggested further learning
Simple recap of Von Neumann Arch:
  http://www.youtube.com/watch?v=DMiEgKZ-qCw
Some history of Von Neumann leading towards his machine: (not examined!)
  “The Greatest Computer Programmer Was Its First”
  http://www.youtube.com/watch?v=Po3vwMq_2xA

## Slide 15: The Harvard Architecture
EEE4084F
Von Neumann
Harvard
The Big Competitor…

## Slide 16: The Harvard Architecture
The Harvard architecture physically separates storage and signal lines for instructions and data.
The term originated from the “Harvard Mark I” relay-based computer that stored instructions on (24-bits wide) punched tape and data in electro-mechanical counters.
Data storage entirely contained within the central processing unit, and provided no access to the instruction storage as data.
(for the original MarkI) programs needed to be loaded by an operator as the processor could not initialize itself.
ALU
Control Unit
Instruction memory
Data memory
I/O
Nowadays this general architecture (albeit greatly enhanced) is still relevant! They are technically referred to as “modified Harvard architecture”. Many processors today (especially embedded ones) still implement this separation of data and storage for performance and reliability reasons.
Harvard Architecture

## Slide 17: The Harvard Mark I
“Harvard Mark I”
https://www.youtube.com/watch?v=4ObouwCHk8w

## Slide 18: Flynns Taxonomy of Processor Architectures
EEE4084F
Type
A
Type
B
Type
C
Type
D
Type
E
Type
F
Type
G
Type
H
Type
I
Type
J

## Slide 19: Flynn’s taxonomy
Flynn’s (1966) taxonomy was developed as a means to classify parallel computer architectures
Computer system can be fit into one of the following four forms:
SISD
Single Instruction Single Data
SIMD
Single Instruction Multiple Data
MISD
Multiple Instructions Single Data
MIMD
Multiple Instructions Multiple Data
Not to be confused with the terms of “Single Program Multiple Data (SPMD)” and “Multiple Program Multiple Data (MPMD)”.
Flynn’s
Taxon.
MI
MD

## Slide 20: Single Instruction Single Data (SISD)
This is (obviously) the classic von Neumann Computer: serial (not parallel) computer, e.g.:
  Old style single core PC CPUs, e.g. i486
Single instruction 
  One instruction stream acted on by the CPU during any one clock cycle
Single data 
  Only one input data stream for any one clock cycle
Deterministic execution
0x1000
LD A,[0x2002]
0x1003
LD B,[0x2004]
0x1006
ADD A,B
0x1007
SHL A,1
0x1008
ST A,[0x2000]
x = 2 * (y + z);

## Slide 21: Single Instruction Multiple Data (SIMD)
A form of parallel computer
  Early supercomputers used this model first
  Nowadays it has become common – e.g., used in modern computers on GPUs
Single instruction 
  All processing units execute the same instruction for any given clock cycle
Multiple data 
  Each processing unit can operate on a different data element
LD AX,[DX+0]
LD BX,[EX+0]
ADD AX,BX
SHL AX,1
ST AX,[CX+0]
y= [1 2 3 4]
z = [2 3 4 5]
x = 2 * (y + z)
…
LD AX,[DX+3]
LD BX,[EX+3]
ADD AX,BX
SHL AX,1
ST AX,[CX+3]
…
…
CPU 1
CPU 4

## Slide 22: Single Instruction Multiple Data (SIMD)
Runs in lockstep (i.e., all elements synchronized)
Works well for algorithms with a lot of regularity; e.g. graphics processing.
Two main types:
  Processor arrays
  Vector pipelines
Still highly deterministic (know the same operation is applied to specific set of data – but more data to keep track of per instruction)

## Slide 23: Single Instruction Multiple Data (SIMD) Examples
Vector pipelines
  IBM 9000, Cray X-MP, Fujitsu vector processor, NEC SX-2, Hitachi S820, ETA10
Processor arrays
  Thinking Machine CM2, MasPar MP-1 & MP-2, ILLIAC IV
Graphics processor units usually use SIMD
Cray X-MP
MasPar MP-1

## Slide 24: Multiple Instruction Single Data (MISD)
Single data stream fed into multiple processing units
Each processing unit works on data independently via independent instruction streams
Few actual examples of this class of parallel computer have ever existed

## Slide 25: Multiple Instruction Single Data (MISD) Example
…
…
…
Possible uses? Somewhat intellectual?
  Maybe redundant! (see next slide)
Possible example application:
  Different set of signal processing operations working the same signal stream
x = +MAXINT
Example:
Simultaneously find the min and max input, and do a sum of inputs.
x = -MAXINT
x = 0
If A<x then x = A
If A>x then x = A
x = x + A
A = input
CPU 1
CPU 2
CPU 3

## Slide 26: Multiple Instruction Multiple Data (MIMD)
The most common type of parallel computer (most late model computers, e.g. Intel Core Duo, in this category)
Multiple Instruction 
  Each processor can be executing a different instruction stream
Multiple Data 
  Every processor may be working with a different data stream
Execution can be asynchronous or synchronous; non-deterministic or deterministic

## Slide 27: Multiple Instruction Multiple Data (MIMD)
Examples
  Many of the current supercomputers
  Networked parallel computer clusters
  SMP computers
  multi-core PCs
MIMD architectures could include all the other models. e.g.,
  SISD – just one CPU active, others running NOP
  SIMD – all CPUs load the same instruction but apply to different data
  MISD – all CPUs load different instructions but apply it to the same data
AMD Opteron
IBM BlueGene

## Slide 28: Class Activity
Consider the types of programming models:
Sequential / non-parallel
Data parallel model
Message passing model
Shared memory model
Hybrid models
Types of architecture models
SISD
Single Instruction Single Data
SIMD
Single Instruction Multiple Data
MISD
Multiple Instructions Single Data
MIMD
Multiple Instructions Multiple Data
Consider an application:
Transaction processing
Face recognition
3D graphics rendering
Pattern search (or string search)
Radar
Database queries
Step 1: choose an application
Step 2: which programming model would you like to use?
Step 3: which computer architecture would you use?
TODO: Work in groups. Follow steps 1-3 shown for a selection of the applications listed in step 1.
We will them vote on the choices.
Your task
(1)
(2)
(3)
(4)

## Slide 29: Voting for Flynn’s
SISD
Single Instruction Single Data
SIMD
Single Instruction Multiple Data
MISD
Multiple Instructions Single Data
MIMD
Multiple Instructions Multiple Data
(1)
(2)
(3)
(4)
Program | SISD(1) | SIMD(2) | MISD(3) | MIMD(4)
Transaction processing |  |  |  | 
Face recognition |  |  |  | 
3D graphics rendering |  |  |  | 
Pattern search |  |  |  | 
Radar |  |  |  | 
Database queries |  |  |  | 
SQ = Sequential / non-parallel
DP = Data parallel model
MP = Message passing model
SM = Shared memory model
HM = Hybrid models
SQ
MH: SM+MP
SM
DP
MP
(MP)
DP
Click to see my suggested answers…
Many of these are somewhat debatable. In a quiz situation it would probably be a good idea to add comments to your answer motivating your choices.

## Slide 30: Memory Architectures & Case Studies of classic micro-controller/processor architectures
EEE4084F
To follow later….

## Slide 31
Long Intermission
Next period:
Considerations of reading based on shared memory and pthreads
“An architecture of on-chip-memory multi-threading processor” by T Matsuzaki, H Tomiyasu and M Amamiya
“Quantifying the Performance Impact of Memory Latency and Bandwidth for Big Data Workloads” by R Clapp, M Dimitrov, K Kumar, V Viswanathan and T Willhalm

## Slide 32: Parallel computer memory architectures
The choice of memory architecture is not necessarily dependent on the ‘Flynn classification’
For a SISM computer, this aspect is largely irrelevant (but consider a PC with GPU and DMA as not being in the SISM category)

## Slide 33: Shared Memory Architecture
EEE4084F
happy memories

## Slide 34: Shared Memory Architectures
Generally, all processors have access to all memory in a global address space.
Processors operate independently, but they can share the same global memory.
Changes to global memory done by one processor are seen by the other processors.
Shared memory machines can be divided into two types, depending on when memory is accessed:
  Uniform Memory Access (UMA) or
  Non-uniform Memory Access (NUMA)

## Slide 35: Uniform Memory Access (UMA)
Common today in form of Symmetric Multi-Processor (SMP) machines
  Identical processors
  Equal access and access times to memory
  Cache coherent
Cache coherent =
    When one processor writes a location in shared memory, all other processors are updated.
    Cache coherency is implemented at the hardware level.
MEMORY
CPU
CPU
CPU
CPU

## Slide 36: Non-Uniform Memory Access (NUMA)
Not all processors have the same access time to all the memories
Memory access across link is slower
If cache coherency is maintained, then may also be called CC-NUMA - Cache Coherent NUMA
CPU
MEMORY
CPU
CPU
MEMORY
CPU
Interconnect bus
SMP 1
SMP 2
This architecture has two SMPs
connected via a bus. When a CPU on SMP1 needs to access memory connected to SMP2, there will be some form of lag which may be a few times slower than access to SMP1’s own memory.

## Slide 37: Shared memory pros & cons
Advantages
  Global address space gives a user-friendly programming approach (as discussed in shared memory programming model)
  Sharing data between tasks is fast and uniform due to the proximity of memory to CPUs
Disadvantages:
  Major drawback: lack of scalability between memory and CPUs.
  Adding CPUs can increases traffic on shared memory-CPU path (for cache coherent systems also increases traffic associated with cache/memory management)

## Slide 38: Shared memory pros & cons
Disadvantages
  Programmer responsible for implementing/using synchronization constructs to make sure that correct access of global memory is done.
  Becomes more difficult and expensive to design and construct shared memory machines with ever increasing numbers of processors.

## Slide 39: Distributed memory architecture
Similar to shared memory, but requires a communications network to share memory
Local Memory
CPU
Communications network
Local Memory
CPU
Local Memory
CPU
…
Each processor has its own local memory (not directly accessible by the other processors’ memory addresses)
Processors connected via a communication network – the communication network fabric varies; could simply be Ethernet.
Cache coherency does not apply (when a CPU changes its local memory, the hardware does not notify the other processors – if needed the programmer needs to provide this functionality)
Programmer responsible for implementing methods by which one processor can access memory of a different processor.

## Slide 40: Distributed Memory architectures: Pros & Cons
Advantages:
  Memory scalable with number of processors
  Each processor can access own memory quickly without communication overheads or maintaining cache coherency (for UMA).
  Cost benefits: use of commercial off-the-shelf (COTS) processors and networks

## Slide 41: Distributed Memory: Pros & Cons
Disadvantages:
  Programmer takes on responsibility for data consistency, synchronization and communication between processors.
  Existing (legacy) programs based on shared global memory may be difficult to port to this model.
  May be more difficult to write applications for distributed memory systems than it is for shared memory systems.
  Restricted by non-uniform memory access (NUMA) performance (meaning a memory access bottle neck that may be many times slower than shared memory systems)

## Slide 42: Distributed Shared Memory (i.e. Hybrid) System
Simply a network of shared memory systems (possibly in one computer or a cluster of separated computers)
Use in many modern supercomputer designs today
Shared memory part is usually UMA (cache coherent)
Pros & Cons? – Best and Worst of two worlds.

## Slide 43: A look at some classic microprocessor architectures
EEE4084F

## Slide 44: The PIC - an 8bit example
Let’s focus in a bit on the main elements…
Q: Architecture type?
A: Harvard (or modified Harvard architecture)

## Slide 45: The PIC - I/O structure
How the IO ports are connected up and interrupt system.

## Slide 46: The AVR tiny84
Q: Architecture type?
A: Harvard (or modified Harvard architecture)
focus in…

## Slide 47: The AVR tiny84 focusing in…

## Slide 48: The 8086
Q: Architecture type?
A: Von Neumann

## Slide 49: Further (more complex) architecture case study
EEE4084F

## Slide 50: Sony Play Station (ver 2)
* Slides adapted from “memory3 case study” by Z. Jerry Shi, University of Connecticut

## Slide 51: Sony Play Station 2 Caches and scratch memory
* Slides adapted from “memory3 case study” by Z. Jerry Shi, University of Connecticut
Somewhat like L1 cache
PS2 has small caches since it was expected the system would be very dynamic and data would not be in the cache for long

## Slide 52: L06 - Linked Reading
Quantifying the Performance Impact of Memory Latency and Bandwidth for Big Data Workloads
R Clapp, M Dimitrov, K Kumar, V Viswanathan and T Willhalm Pub date: 2005
In recent years, DRAM technology improvements have scaled at a much slower pace than processors. While server processor core counts grow from 33% to 50% on a yearly cadence, DDR 3/4 memory channel bandwidth has grown at a slower rate, and memory latency has remained relatively ﬂat for some time. Combined with new computing paradigms such as big data analytics, which involves analyzing massive volumes of data in real time, there is a trend of increasing pressure on the memory subsystem. This makes it important for computer architects to understand the sensitivity of the performance of big data workloads to memory bandwidth and latency, and how these workloads compare to more conventional workloads. To address this, we present straightforward analytic equations to quantify the impact of memory bandwidth and latency on workload performance, leveraging measured data from performance counters on real systems. We demonstrate how the values of the components of these equations can be used to classify diﬀerent workloads according to their inherent bandwidth requirement and latency sensitivity. Using this performance model, we show the relative sensitivities of big data, high-performance computing, and enterprise workload classes to changes in memory bandwidth and latency.
File: 07314167.pdf
http://dx.doi.org/10.1109/IISWC.2015.32
This paper gives a useful insights into memory architectures in relation to big data processing. Note re studying this paper: the different classifications of workload models don’t need to be remembered for tests etc, you’d be given a scenario description; the useful learning is more insights into approaches for the different scenarios presented.

## Slide 53: L06 - Linked Reading
An architecture of on-chip-memory multi-threading processor
T Matsuzaki, H Tomiyasu and M Amamiya Pub date: 2001
This paper proposes an on-chip-memory processor architecture: FUCE. FUCE means Fusion of Communication and Execution. The goal of the FUCE processor project is fusing the intra processor execution and inter processor communication. In order to achieve this goal, the FUCE processor integrates the processor units, memory units and communication units into a chip. FUCE Processor provides a next generation memory system architecture. In this architecture, no data cache memory is required, since memory access latency can be hidden due to the simultaneous multithreading mechanism and the on-chip-memory system with broad-bandwidth low latency internal bus of FUCE Processor. This approach can reduce the performance gap between instruction execution, and memory and network accesses.
File: 00955202.pdf
http://dx.doi.org/10.1109/IWIA.2001.955202
This paper gives a useful case study discussing the FUCE processor. I recommend have a brief look through this paper to get a sense of the architecture and particularly the approach these authors take to explain their design and discuss the performance of the system. Unlikely any test/exam questions would ask specific questions about this paper/ archtitecture

## Slide 54
Image sources:
Stop watch slides 1 & 14, Gold bar: Wikipedia (open commons)
books clipart: http://www.clker.com (open commons)
Disclaimers and copyright/licensing details
I have tried to follow the correct practices concerning copyright and licensing of material, particularly image sources that have been used in this presentation. I have put much effort into trying to make this material open access so that it can be of benefit to others in their teaching and learning practice. Any mistakes or omissions with regards to these issues I will correct when notified. To the best of my understanding the material in these slides can be shared according to the Creative Commons “Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)” license, and that is why I selected that license to apply to this presentation (it’s not because I particulate want my slides referenced but more to acknowledge the sources and generosity of others who have provided free material such as the images I have used).