## Slide 1
Lecture 23
Softcore Processors
Lecturer:
Simon Winberg
Digital Systems
EEE4084F
Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)
soft
processor

## Slide 2: Lecture Overview
Softcore processors
Case studies:
  Xilinx Microblaze
  Xilinx Picoblaze
  DUGONG (a simplified ‘sort of’ interface control processor)
  [Optional: Altera/Intel NIOS2]

## Slide 3: Softcore processors
EEE4084F

## Slide 4: Soft core Processors: Processors within FPGAs
What is a ‘soft core’?
  A soft microprocessor is a microprocessor core that can be wholly implemented using logic synthesis.
  It is essentially an item of ‘Intellectual Property’ (IP) that contains the design of a processor.
  A soft core processors can be incorporated into a design and then the design synthesized, place & routed to generate an executable.
  Examples of these:
    Altera NIOS II
    Xilinx Microblaze & Xilinx Picoblaze
    A variety of ARM processors
How do these compare to hard cores? … see later!

## Slide 5: How a Soft core typically fits in to a design
Soft Core Processor
FPGA
Avalon bus for NIOS,
OPB (Onchip Peripheral Bus) or PLB (Processor Local Bus) for Microblaze

## Slide 6: Address Bus for the Processor
FFT Engine
Timer
GPIO
Eth MAC
VGA
… etc …

## Slide 7: Ingredients Needed for Soft Cores
Could implement it all as gates, but that can be rather inefficient and wasteful
On-chip resources that soft core processors typically use:
  RAM blocks - various configurations
  Full adders
  DSP cores (e.g. integer multipliers, etc.)
  State machines

## Slide 8: Hard core vs. Soft core ?!
Softcore =
Lite/Easy??
Hardcore =
Difficult??
Not necessarily…

## Slide 9: Hard Core Processor Characteristics
Not implemented as gateware programmed into the FPGA logic
Implemented in silicon/ASIC; unchangeable
Benefits:
  Usually much higher performance
  Manufacturer typically provides optimized compiler for their chips

## Slide 10: Reading (supplementary, not examined)
“A Dual-Issue Embedded Processor for Low Power Devices” by H Lozano, M Ito
The authors propose “an energy efficient dual-issue embedded processor that can deliver up to 60% improvement in IPC (instruction-per-cycle)…”
Paper L21 - 07157822 - Dual-Issue Embedded Processor for Low Power Devices.pdf
http://dx.doi.org/10.4108/icst.iniscom.2015.258414

## Slide 11: Case Studies (shortly)
MicroBlaze
  32-bit processor, RISC instructions.
  Thirty-two 32-bit general purpose registers
  Generate, configure and program with Xilinx SDK
Picoblaze
  8 bit, simple RISC instructions
  Free for use on Xilinx
DUGONG (a scenario showing example developed by a UCT student, a state machine with instructions)
  Planning to be control module
  Open-source
NIOS II
  Altera’s soft core processor, 32 bit, configurable
  Commercial
  NIOS II Gen2 improved, more options
  Alternate soft cores: MP32 / MIPS32, ARM
Simpler, closer to simple FSM
More powerful, closer to full CPU
NIOS is recommended additional reading (it is an Altera/Intel product)

## Slide 12: Considerations for Using Soft Core Processors
A major purpose is:
  Make it easier to communicate / transfer & packetize data
  Test designs (e.g. like reading/adjusting setting while running)
  Set up the initial conditions of your design / HDL block configuration
  Highly configurable processor structure – e.g. add a custom instruction to baseline processor
  Of course also e.g. testing novel processor designs
Should consider the soft core processor is
  More an aid to control the system
    facilitate comms, advantages of software running in system, e.g. O/S
The soft core processor shouldn’t
  Be provide the main solution to you digital accelerator, unless there is good reason such as experimenting with performance of a cluster of processors on FPGA
First two points are most common use

## Slide 13: Optional Case Study
NIOS II
  Altera’s soft core processor, 32 bit, configurable
  Commercial
  NIOS II Gen2 improved, more options
  Alternate soft cores: MP32 / MIPS32, ARM
More powerful, closer to full CPU
NIOS is recommended additional reading, see last slides
It is an Altera/Intel product

## Slide 14: Soft Core Case Studies
PicoBlaze
Xilinx
MicroBlaze
DUGONG
(Open source)

## Slide 15: Xilinx Microblaze
MicroBlaze was developed by Xilinx
It is a soft microprocessor core designed and optimized for use on Xilinx FPGAs
MicroBlaze is a Reduced Instruction Set Computer (RISC)
Generated, configured and programmed using Xilinx EDK (Embedded Development Kit)

## Slide 16: FPGAs that support Microblaze
You can’t run it on any FPGA!! It works on only supported those Xilinx FPGAs. These include the FPGAs families:
  Spartan-3/3A/3AN/3A DSP/3E FPGA
  Spartan-6
  Virtex-4 FX (also supports PowerPC 405 processors) and LX/SX FPGA
  Virtex-5 FXT (alost PowerPC 440 processor) LX/LXT FPGA (MicroBlaze)
  Virtex-6 (MicroBlaze processor)

## Slide 17: Microblaze and its surrounding components
Supports two bus Standards:
PLB (Processor Local Bus) (ver. V46)
  for high speed & high bandwidth peripherals.
  Supports 128 bits of data, 36 bit address
XILINX Local Memory Bus (LMB) to interface local PLBs

## Slide 18: MicroBlaze memory
Cache
  By default MicroBlaze has no cache.
  Can enable cache in EDK (which will use BRAM)

## Slide 19: MicroBlaze Architecture

## Slide 20: Features
Highly configurable soft processor
Can select a specific set of features needed
Fixed features of the processor are:
  Thirty-two 32-bit general purpose registers
  32-bit instruction word with three operands and two addressing modes
  32-bit address bus
  Single issue pipeline
The MicroBlaze can be parameterized to enable inclusion of additional functionality.

## Slide 21: MicroBlaze instructions
The MicroBlaze has a versatile interconnect system to support a variety of embedded applications.
MicroBlaze instruction set is similar to that of the RISC-based DLX architecture.
Most vendor-supplied and third-party IP modules interface to PLB directly (or through an PLB to OPB bus bridge.)
For access to local-memory (BRAM in the FPGA), the MicroBlaze uses a dedicated LMB bus that reduces loading on the other buses (e.g. OPB).
User-defined coprocessors are supported through a dedicated FIFO-style connection called FSL (Fast Simplex Link).
The coprocessor(s) interface can accelerate computationally intensive algorithms by offloading parts or the entirety of the computation to a user-designed hardware module.

## Slide 22: Microblaze
High performance soft processor
  Most of instructions completed with 1 cycles
  Short pipelines, higher working frequency
  FPGA optimized implementation
    Fast carry chain MUX, hardware multiplier
    RLOC placement constraints
Easy (relatively) to use with Xilinx EDK
  Linux/GCC support

## Slide 23: MicroBlaze Limitations
No MMU support
  No protection among processes
  Implies it cannot support full version of Linux
No double precision floating point
No atomic instructions
  hard to implement lock
  non-blocking FIFO instruction problem
No cache coherent support

## Slide 24: Micro MicroBlaze
A smaller, but powerful MicroBalze:
The MicroBlaze MicroController System (MCS)
  MCS offers an even smaller package
  MCS consists of MicroBlaze in a fixed 3-stage pipeline configuration for the smallest footprint, and is surrounded by a system of common embedded design peripherals*.
* MCS can run from IDS Logic Edition without the need for a full embedded design license

## Slide 25: MicroBlaze – references & where to find out more
Xilinx MicroBlaze Wiki
  http://www.wiki.xilinx.com/MicroBlaze
Wikipedia
  https://en.wikipedia.org/wiki/MicroBlaze
Building an embedded system using a Microblaze on an Nexys3
  http://islab.soe.uoguelph.ca/sareibi/TEACHING_dr/XILINX_TUTORIALS_dr/EDK_dr/EDK-NEXYS3-Elhossini2012.pdf
Some of the information regarding MicroBlaze based on slides by K. Siddhapathak

## Slide 26: Soft Core Case Studies
PicoBlaze
Xilinx
MicroBlaze
DUGONG
(Open source)

## Slide 27: PicoBlaze Soft Core Processor
Size:
  Takes on 96 slices !! (slice = group of PLBs)
  Big advantage considering low cost FPGAs have a few 100 slices; and 1000s slices for medium range
Not coded as behavioral VHDL
  It is manually pre-compiled (IP block)
  Built by instantiation of Xilinx raw primitives
  Can still be simulated using Modelsim
Info available from: www.xilinx.com/picoblaze

## Slide 28: PicoBlaze Soft Core Processor
Main Uses
  Control / configuration of parameters
  Some data processing (add / integer operations)
  Comms / UI facilities (i.e. ‘talk’ to control PC, especially UART, USB connection)
  Testing & debugging your design on hardware

## Slide 29: PicoBlaze Soft Core Processor
Can be very helpful to speed-up & simplify development
  Changing the instructions running on the softcore PicoBlaze is likely faster than changing the HDL code (especially with rebuilding time)
  Has a simple and easy to learn instruction set, also offers opportunities for reuse of the PicoBlaze code in other systems.

## Slide 30
PicoBlaze
Architecture

## Slide 31: Overview of the PicoBlaze

## Slide 32: Interfacing to the PicoBlaze
clock
PicoBlaze
KCPSM = constant (K) Coded Programmable State Machine

## Slide 33: PicoBlaze Interface
Name | Direction | Size | Function
clk | input | 1 | System clock signal in
reset | input | 1 | Reset signal
address | output | 10 | Address of instruction mem. Specifies address of the instruction to be retrieved.
Instruction | input | 18 | Fetched instruction.
port_id | output | 8 | Address of the input or output port.
in_port | input | 8 | Input data from I/O peripherals.
read_strobe | output | 1 | Strobe associated with the input operation.
out_port | output | 8 | Output data to I/O peripherals.
write_strobe | output | 1 | Strobe associated with the output operation.
interrupt | input | 1 | Interrupt request from I/O peripherals.
interrupt_ack | output | 1 | Interrupt acknowledgment to I/O peripherals

## Slide 34: PicoBlaze Addressing Modes
Direct mode
INPUT s5, 2a
ADD sa, sf
PORT[2a] s5
sa + sf  sa
Indirect mode
INPUT s9, (s2)
STORE s3, (sa)
PORT[RAM[s2]]s9
s3 RAM[RAM[sa]]
s2+08+C  s2
s7–7  s7
Immediate mode
ADDCY s2,08
SUB s7, 7
Instruction example
Explanation

## Slide 35: Example Program
; DEMONSTRATION PROGRAM
; EXERCISE THE 7 SEGMENT DISPLAYS
cold_start:
LOAD s3, 11 ; clear all time values
OUTPUT s3, 04
LOAD s4, 00
OUTPUT s4, 05
main_loop:
OUTPUT s5,04 ; Update 4 digit 7 seg display
OUTPUT s3,06
JUMP main_loop

## Slide 36: Soft Core Case Studies
Nios II
PicoBlaze
Xilinx
DUGONG
(Open source)

## Slide 37: Why look at this one
This provides a case study of a custom-designed processor which provides a variety of useful facilities that are useful especially in configuring other modules in an FPGA, or being used as a junction for moving data around within the FPGA or steering the data to e.g. an output port or for doing debug inspections (kind of like a boot monitor for an FPGA; you can send it various commands – in machine language – and it can carry them out to do inspections on the modules running in the system)

## Slide 38: DUGONG
Developed by Matthew Bridges (SDRG student), part of a larger research project
Designed from scratch (a solution to a need)
Design around compatibility with Wishbone interface
Designed with a focus on simplicity with scalability
But what is it???
Available at:
https://github.com/matthewbridges/dugong

## Slide 39: ‘DUGONG’ name?
A dugong is actually a type of underwater mammal, colloquially called ‘sea cow’ that is found in the Indian Ocean (similarities to ‘manatees’)
The DUGONG controller was given this name as it’s a ‘underwater’ hidden feature, and no one else is likely to choose the name… and it is a kind of grazer like a RHINO

## Slide 40: DUGONG
Essentially it is a glorified state machine
But has limited number of states and transition types (i.e. predefined list of triggers, operations, transitions, etc.)

## Slide 41: DUGONG
Essentially it is a glorified state machine
Works as follows:
  A list of timing and transfer operations are loaded into it, and it runs through these sequentially
OP1
OP2
OP3
Data in
OP1
OP2
OP3
Send
config
Redirect mode
Config mode
MODES:
Various other modes, some simultaneous.

## Slide 42: DUGONG Structure
WISHBONE
Has one register, the accumulator, through which data is transferred.
To control processor interface (GPMC bus on RHINO)

## Slide 43: Connecting to DUGONG
Serves as the Master on the wishbone bus
Wishbone bus: Open source hardware interconnect bus structure for connecting computational blocks within ICs / reconfigurable computers. This bus structure is commonly used by designs provided by OpenCores.
Wishbone interfaces for Master and Slave modules

## Slide 44: How DUGONG fits in to a Wishbone-based design
Controls the wishbone clock lines, etc.

## Slide 45: DUGONG
Designed around simplicity & scalability (connect up and configure small to big designs)
Has no function unit (FU) – with good reason
Can I use it for processing? Comparisons?
  Sorry, no can do: that is someone else's problem (or rather use a CPU e.g. Nios II)
OpenCores.org: http://opencores.org/
Open Hardware Repository: http://www.ohwr.org/
There are lots of other opensource soft cores available, see e.g.:

## Slide 46: DUGONG Instruction Set
DUGONG1:
  4 bit Instruction Set
  Structure: <CODE:4 bits> <DATA:28 bits>
Code | Instruction | Description
0000 | NOP | No operation
0001 | WRITE | Write data to addr
0010 | READA | Read from addr to acc
0011 | WRITEA | Write from acc to addr
0100 | BRANCH | write data to pc / controller
1000 | WAIT | Wait for a number of clock cycles equal to data field

## Slide 47: DUGONG Typical Program
WRITE #0, [0xFF000000] // write 0 to address
READA [0xFF100000] // read from addr into A
WAIT #4 // wait for 4 clock cycles
WRITEA [0xFF200000] // write A to addr
BRANCH // send data in A to controller
NOP
NOP …

## Slide 48
Q & A

## Slide 49: Soft Core Case Studies
Nios II
PicoBlaze
Xilinx
DUGONG
(Open source)

## Slide 50: Altera Nios II Processor
A 32-bit soft core processor from Altera
Three standard cores versions:
  Fast, Standard, Light
The cores have tradeoffs in:
  FPGA LEs needed  power  speed
RISC architecture: Simple instructions
Harvard Architecture:
  Separated data and instruction memories (a likely safer approach to the Von Neumann arch. style)
32 interrupt levels
Avalon Bus interface
C/C++ compilers; can also use plain assembly

## Slide 51: NIOS II Architecture
Image source: www.altera.com
Let’s have a closer look at the core

## Slide 52: NIOS II Core

## Slide 53
How do you get a NIOS II soft core processor and set it up?

## Slide 54: Altera Qsys: In later versions of Quartus II
1. Select Tools
2. Select Qsys

## Slide 55
1. Select Tools
2. Select SOPC Builder
Altera SOPC Builder: In earlier versions of Quartus II

## Slide 56: Altera QSys

## Slide 57
Image sources:
man working on laptop – flickr
scroll, video reel, big question mark – Pixabay http://pixabay.com/ (public domain)
some diagrammatic elements are from Xilinx ISE screenshots
https://commons.wikimedia.org/wiki/Category:Images (creative commons)
Disclaimers and copyright/licensing details
I have tried to follow the correct practices concerning copyright and licensing of material, particularly image sources that have been used in this presentation. I have put much effort into trying to make this material open access so that it can be of benefit to others in their teaching and learning practice. Any mistakes or omissions with regards to these issues I will correct when notified. To the best of my understanding the material in these slides can be shared according to the Creative Commons “Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)” license, and that is why I selected that license to apply to this presentation (it’s not because I particularly want my slides referenced but more to acknowledge the sources and generosity of others who have provided free material such as the images I have used).