## Slide 1
Lect2: Terms, Golden Measure Prac1 Preparation
Lecturer:
Simon Winberg
Digital Systems
EEE4084F
Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)

## Slide 2: Outline for Lecture
Terms
Validation vs. Verification
Commonly used verification methods
Class Activity – Quiz#0
Prac 1
Latex

## Slide 3
TERMS
TRENDS

## Slide 4: Terms
Golden measure:
  A (usually) sequential solution that you develop as the ‘yard stick’
  A solution that may run slowly, isn’t optimized, but you know it gives (numerically speaking) excellent results
  E.g., a solution written in OCTAVE or MatLab, verify it is correct using graphs, inspecting values, checking by hand with calculator, etc.
Discussed a bit more later…

## Slide 5: Terms
Sequential / Serial (serial.c)
  A non-parallized code solution
Generally, you can call your code solutions parallel.c (or para1.c, para2.c if you have multiple versions)
You can also include some test data (if it isn’t too big, <1Mb), e.g. gold.csv or serial.csv, and paral1.csv

## Slide 6: Speed-up
Speed-up = Tp1 /Tp2
Where Tp1 = Run-time of original (or non-optimized) program
Tp2 = Run-time of optimised program
Best practice for measuring speedup:
  Run the program more than one, discarding the first result (where the cache, etc. is getting ‘warmed up’)
  To be precise should indicate results from when system wasn’t ‘warmed up’*
* (which can be simulated by running a whole lot of other things like CounterStrike, Half-Life, maybe some Solitare* for good measure -- but more seriously you could write your own ‘cache cleaning program’)

## Slide 7: Speed-up graphs

## Slide 8: Other Important Terms
Verification
Validation
Testing
Correctness proof
These terms are not merely theoretical terms to remember, but relate directly to your project.
Not something done in the project (but if you want to, you can experiment with doing a correctness proof if you are keen)

## Slide 9: Verification and Validation (V&V)
Two terms you should already know…
Verification
  “Are we building the product right?”
  Have we made what we understood we wanted to make?
  Does the product satisfy its specifications?
Validation
  “Are we building the right product?”
  Does the product satisfy the users’ requirements
Verification before validation (except in duress)…
Sommerville, I. Software Engineering. Addison-Wesley, 2000.
  While it would be nice to be able to validate before verifying, doing so would mean your specifications and design may be wrong in the final version (obviously this sometimes happens in practice due to insufficient time for proper validation)

## Slide 10: Verification before validation
The RC engineer (i.e., you) are effectively designing both custom hardware and custom software for the RC platform
Before attempting to make claims about the validity of your system, it’s usually best practice to establish your own (or team’s) confidence in what your system is doing, i.e. be sure that:
  The custom hardware working;
  The software implementation is doing what it was designed to do; and
  The custom software runs reliably on the custom hardware.

## Slide 11: Verification
Checking plans, documents, code, requirements and specifications
Is everything that you need there?
Algorithms/functions working properly?
Done during phase interval (e.g., design => implementation)
Activities:
  Review meetings, walkthroughs, inspections
  Informal demonstrations
Focus of
project
Focus of project

## Slide 12: Commonly used verification methods
Dual processing, producing two result sets
  One version using PC & simulation only;
  Other version including RC platform
Assume the PC version is the correct one (i.e., the gold measure)
Correlate the results to establish correlation coefficients
  (complex systems may have many different sets of possibly multidimensional data that need to be compared)
The correlation coefficients can be used as a kind of ‘confidence factor’

## Slide 13: Validation
Testing of the whole product / system
Input: checklist of things to test or list of issues that need to have been provided/fixed
Towards end of project
Activities:
  Formal demonstrations
  Factory Acceptance Test
Focus of project

## Slide 14: Testing and Correctness proofs
Testing
  Generally refers to aspects of dynamic validation in which a program is executed and the results analysed
Correctness proofs / formal verification
  More a mathematical approach
  Exhaustive test => specification guaranteed correct
  Formal verification of hardware is especially relevant to RC. Formal methods include:
    Model checking / state space exploration
    Use of linear temporal logic and computational tree logic
    Mathematical proof (e.g. proof by induction)

## Slide 15: TODO …
EEE4084F Digital Systems

## Slide 16: Class Activity
Quiz #0 - “Initial impressions”
10 minutes to complete a few simple survey questions and prerequisite tests.
This quiz is not for marks
Name & student number voluntary

## Slide 17: Marking of Quiz0?
Please hand back your Quiz0
Next lecture I’ll show you the correct solutions  (or if you are impatient, which is partly why I set the quiz, you can search for answers online and at the same time probably encounter other interesting computing terms).

## Slide 18: PRAC1
Using OCTAVE

## Slide 19: Planning for 20-24 Mar
Prac1 avail for you to work on. Experiment with C or OCTAVE (note includes a report that is for marks and to be submitted online using Vula)
3pm afternoon lecture today:
  to cover Terms, Amdahl's Law etc.

## Slide 20: Prac1: OCTAVE & Correlations
See Assignments on the course website
See you all on Monday 9am
rem.
to do
h/w
http://www.rrsg.ee.uct.ac.za/courses/EEE4084F/Practicals.html

## Slide 21: Towards Prac1
Prac1 involves OCTAVE
OCTAVE is like a free version of MATLAB
You can install OCTAVE on your own PC you you’d like to see:
  https://www.gnu.org/software/octave/download.html
A suggested OCTAVE tutorial to help you prepare for Prac1
    Brief intro to OCTAVE: https://www.gnu.org/software/octave/doc/v4.0.0/Introduction.html

## Slide 22: Parts of the Pracs
Initial Parts (e.g. Part A)
  Example program that helps get you started quicker
Subsequent Parts
  The main part, where you provide a parallelized solution

## Slide 23: Prac1: Why OCTAVE
The idea of starting you out with OCTAVE is that it is a useful (free!) tool that you can use later, e.g. in further pracs to verify calculations etc.

## Slide 24: Prac 1
Contains 4 parts
  Part 1: Starting out in OCTAVE, generating matrices, doing plots, saving data
  Part 2: Working with ﬁles
  Part 3: Measuring execution time with tic and toc
  Part 4: Implementing a Correlation routine
What to hand in
  Hand in a short report brieﬂy describing your solutions for Part 3 step #4 and Part 4

## Slide 25: Prac Reports
EEE4084F

## Slide 26: Using Latex
For Prac 1 you’re all expected to use Latex.
  Use TexStudio or TexMaker, these are easy to use tools for writing documents in latex.
It is quite straightforward unless you want to do fancy things, such as
  Adding equations
  Positioning text in non-standard ways (e.g. indenting)
  Getting images / tables / listings to be where you want them (as opposed to where Latex decides they should be placed).
  With some practice you’ll see it isn’t so difficult and could actually be a big help in the longrun for example for writing your BSc final year project report.

## Slide 27: TexStudio – suggested tool to use!

## Slide 28
Brief
Demo
Using TexStudio

## Slide 29: Latex Help
Latex Stack Exchange
  http://tex.stackexchange.com/
  This is essentially the go-to place for help in solving Latex problems easy or hard.
Online manuals/guide
  Tobias Oetiker's Guide to Latex
  Latex WikiBook:
    https://en.wikibooks.org/wiki/LaTeX

## Slide 30: Correlation recap
EEE4084F

## Slide 31: Why is Correlation important in this course?
Correlation is used as a means to objectively tell how accurate your experimental solution is measured against a known good solution (the Golden Measure)
Typically used to get a sense (confirm) that your experimental system is adequately correct

## Slide 32: Correlation
Finding the relationship between two quantitative variables, e.g. the price of cheese to the age of cheese.
Correlation is a statistical technique used to determine the degree to which two variables are related

## Slide 33: Correlation
Looking at a scatter diagram gives an impression of how variables are related…
Straight line linear regression
What has the cost of cheese got to do with its age?

## Slide 34: Correlation
The pattern of data is indicative of the type of relationship between your two variables:
  positive relationship
  negative relationship
  No / minimal relationship

## Slide 35: Correlation Relations
Positive Relation
Negative Relation
No Relation

## Slide 36: Correlation Coefficient (r)
It measures the nature and strength between the variables.
The sign of r denotes the nature of the relationship
  +’ve : direct relation (increase of the one variable leads to increase of the other)
  -’ve: indirect relation (increase of the one variable leads to decrease of the other)
The magnitude denotes the strength of the relationship
  Between 1 (strong) and 0 (week/none)

## Slide 37: Computing the correlation coefficient
Computation of correlations
You can calculate it in one pass through the data… i.e.
sum up x, y, xy, x2 and y2

## Slide 38: Multiple Dimension Correlation
Usually use a table, do correlations between two of the variables for all possible combinations…
 | Weight | Age | Cost
Weight | 1 | 0.02 | 0.81
Age | 0.02 | 1 | 0.65
Cost | 0.81 | 0.65 | 1
symmetric matrix likely to result
What has the cost of cheese got to do with its weight & age

## Slide 39: Simple benchmarking
Using tic and toc in OCTAVE
tic : starts the performance timer
toc : returns the elapsed time since tic was invoked.
Best practice:
  It’s recommendable to use tic and toc in a M file
  It’s a little more accurate if you have tic on the same line as the first instruction to time: i.e.
    tic; do_something; t=toc

## Slide 40: Some sample reports
EEE4084F

## Slide 41
Prac1:
Over to you to make a start!

## Slide 42
End of Lecture 2