## Slide 1
Lecture 4:
Parallel Languages, Automatic Parallelization,
Performance Benchmarking, Metrics of Performance
Presented by
Simon Winberg
Digital Systems
EEE4084F
Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)

## Slide 2: Lecture Overview
Parallel computing programming
Automatic parallelism
Performance benchmarking
Trends

## Slide 3: Software development for parallel computers
Important software sections (frequently run sections) usually hand-crafted , often from initial sequential versions, to run on the parallel computing platform
Why this happens:
  Parallel programming is difficult
  Parallel programs run poorly on sequential machines (need to simulate them)
  Automatic parallelization difficult (& messy)
Leads to high utilization expenses

## Slide 4: Do parallel languages and compilers exist?
Yes!
… some other examples…

## Slide 5: L04 - Further Reading
Parallel and Distributed Computing: Memories of Time Past and a Glimpse at the Future
Author: D C Marinescu. Pub date: June 2014
We propose to look at the evolution of ideas related to parallel systems, algorithms, and applications during the past three decades and then glimpse at the future. The journey starts with massively parallel systems of the early nineties, transitions gently to computing for the masses on the clouds of the ﬁrst decade of the new millennium, and continues with what we could expect from quantum computers and quantum parallelism in the next few decades...
File: 06900194.pdf
http://dx.doi.org/10.1109/ISPDC.2014.33
This paper gives good insight into the current state of the art and likely approaches that will be used in the future

## Slide 6: Do parallel languages and compilers exist?
Yes!
  MatLab, Simulink, SystemC, UML*, NESL** and others
“Automatic parallelization”:
  Def: converting sequential code into multi-threaded or vectorised code (or both) to utilize multiple processors simultaneously (e.g., for SMP machine)
  … short powwow on the topic…
* Model-Driven Development using case tools, e.g. Rhapsody for RT-UML
Try interactive tutorial on: http://www.cs.cmu.edu/~scandal/nesl/tutorial2.html

## Slide 7: Powwow* moment
Consult the four winds, and your neighbouring classmates, as to: Why is it probably not easy to automate conversion from sequential code (e.g. BASIC or std C program) to parallel code?
HINT: Perhaps start by clarifying the difference between sequential and parallel code.
PS: You’re also welcome to get up, stretch, move about, infiltrate your choice of tribe, and so on. Note approx. 5 min. time limit!
Time
limit
TIME
UP
Next slide provides some reasons...
* It’s a term from North America's Native people used to refer to a cultural gathering.

## Slide 8: Return from the Powwow
What the winds decree…

## Slide 9: Some thoughts
Data hazards
Timing issues
Deciding how to break-up data to distribute
Deciding when to implement semaphores and locks
When code needs to block and when not
How to split-up a loop into parallel parts
Having to convert clocks of statements
or functions in inter process calls
Figuring out timing dependencies
Difficulty in figuring out data dependencies
On why is it probably not easy to automate conversion from sequential code (e.g. BASIC or C) to parallel code.
What the wind has
to say…

## Slide 10: Why automatic parallelism isn’t “quite there yet”
Accumulation of 30+ years of research…
Only limited success in parallelism detection and program transformations
  Instruction-level parallelism at the basic-block level (e.g., pipelining of instructions)
  Parallelism in nested for-loops containing arrays with simple index expressions
  Analysis methods: data dependence analysis, pointer analysis, abstraction back to more optimized implementation, flow analysis

## Slide 11: Why automatic parallelism isn’t “quite there yet”
Main reasons (user perspective):
  Tends to take too long.
  Tend to be too fragile (i.e., breaks down after small changes to the code).
  Tends to miss many things a human would notice and provide an effective solution for, i.e., human intellect, underlying knowledgeable of the application, and trained to write and problem-solve parallel code.
So: Instead of training compilers to recognize parallelism, people are being trained to write parallel code (i.e., no “middle man” approach).

## Slide 12: Temporal and Spatial Computation
Temporal Computation
Spatial Computation
The traditional paradigm
Typical of Programmers
Things done over time steps
Suited to hardware
Possibly more intuitive?
Things related in a space
A = input(“A= ? ”);
B = input(“B =? ”);
C = input(“B multiplier ?”);
X = A + B * C
Y = A – B * C
A?
B?
C?
+
*
X !
Y !
-
Which do you think is easier to make sense of?
Can provide a clearer indication of relative dependencies.

## Slide 13: “Extracting concurrency”
Being able to comprehend and extract the parallelism, or properties of concurrency, from a process or algorithm is essential to accelerating computation
The Reconfigurable Computing (RC) Advantage:
  The computer platform able to adapt according to the concurrency inherent in a particular application in order to accelerate computation for the specific application

## Slide 14: Performance Benchmarking
“Don’t loose sight of the forest for the trees…”
Generally, the main objective is to make the system faster, use less power, use less resources…
Most code doesn’t need to be parallel.
Important questions are…

## Slide 15: Important questions
Should you bother to design a parallel algorithm?
Is your parallel solution better than a simpler approach, especially if that approach is easier to read and share?
Major telling factor is:
Real-time performance measure
Or “wall clock time”

## Slide 16: Benchmarking
EEE4084F

## Slide 17: Benchmarking
Process of measuring performance of a digital system
A program (or systematic approach) that Quantitatively evaluates performance, cost and computer hardware and software resources (among other things) of a computing solution
Benchmark suites – sets of benchmark programs designed to get a comprehensive view of the performance of a computer system for executing a variety of representative processing operations.
Suitable benchmark
  A meaningful representation of what the system can do
  Helps select of an effective system
  Indicates a measure of what one system can do compared to other options
MIPS

## Slide 18: Wall clock time
Generally the most accurate: use built in timer, which is directly related to real time (e.g., if the timer measures 1s, then 1s elapsed in the real world)
Technique:
  unsigned long long start; // store start time
  unsigned long long end; // store end time
  start = read_the_timer(); // e.g. time()
  DO PROCESSNG
  end = read_the_timer(); // e.g. time()
  .. Output the time measurement (end-start), or save it to an array if printing will interfere with the times. Note: to avoid overflow, used unsigned vars.
See file:
Cycle.c

## Slide 19: StdC: gettimeofday
gettimeofday
  Very portable, part of the StdC library
  Should be available on any Linux system
  Returns time in seconds and microseconds since midnight January 1 1970
  Uses struct timeval comprising
    tv_sec : number of seconds
    tv_usec : number of microseconds*
  Converting to microseconds will use huge numbers, rather work on differences
* Word of caution: some implementations always return 0 for the usec field!!
On Cygwin, the resolution is only in milliseconds, so tv_usec in multiples of 1000.
Not provided in DevC++.

## Slide 20: gettimeofday example
#include <stdio.h>
#include <sys/time.h>
#include <time.h>
struct timeval start_time, end_time; // variables to hold start and end time
int main() {
int tot_usecs;
int i,j,sum=0;
gettimeofday(&start_time, (struct timezone*)0); // starting timestamp
/* do some work */
for (i=0; i<10000; i++)
for (j=0; j<i; j++) sum += i*j;
gettimeofday(&end_time, (struct timezone*)0); // ending timestamp
tot_usecs = (end_time.tv_sec-start_time.tv_sec) * 1000000 +
(end_time.tv_usec-start_time.tv_usec);
printf("Total time: %d usec.\n", tot_usecs);
}
See timing.c code file

## Slide 21: What is wrong about using only wall clock time?
It can provide a false impression of how effectively your solution is – at least doesn’t give a ‘full picture’ …
  Typically do tests after the system has ‘warmed up’ (cache loaded) by running the same data multiple times
  May show the solution is quicker… but at what costs? e.g.:
    Speed improved but accuracy sacrificed?
    Development effort vs. execution speed improvement?
    Resource costs for upgrading vs. costs saved by remaining with the old version?
    Power usage? Does the new solution need more power (per execution, also on average including idle time)
    Maintainability? (e.g. is the new version more complex?)
    Environment impact? (Does the upgrade result in waste that could be environmentally detrimental)

## Slide 22: Benchmarking: what to test
What can be benchmarked? For DSP and HPC…
Compiler
  Converts High Level Language to Assembly language thus we benchmark compiler efficiency, such as how efficient is the generated assembly code?
The Processor
  Code in hand-crafted/inspected assembly (to make comparisons fair)
Operating System
  Interrupt latencies, overhead of operating system calls, limits on devices, kernel size, availability of services and facilities such as support for virtual memory and paged memory.
Platform
  Scalability of memory. Peripheral limits. Interfaces supported. Power use. Power saving features. OS’s supported.
Applications (e.g. representative operations for certain application domains – think ‘DWARFS’ as in Berkeley paper)

## Slide 23: Benchmarking: what is usually measured
For DSP/HPEC systems we typically benchmark:
  Cycle count
  Data and Program memory usage
  Execution time
  Power consumption (has recently become a common thing to report on)

## Slide 24: Metrics of Performance
Application
  Operations per second
Programming language
  Expressiveness*
  Code density
Processing system
  MIPS: Million Instructions Per Second GIPS: Giga (i.e. 109) IPS
  MFLOPS: Million FLoating point OPerations per Second GFLOPS: Giga (109) FLOPS TFLOPS: Terra (1012) FLOPS
Datapath
  MBps: Megabytes per second
Function unit / processor hardware
  Cycles per second (clock rate)
* Felleisen, M., 1991. On the expressive power of programming languages.Science of computer programming, 17(1-3), pp.35-75.

## Slide 25: Aspects of CPU Performance
 | Instruction Count (IC) | Cycles Per Instruction (CPI) | Clock
Rate Program |  |  | 
Computer |  |  | 
Instruction Set |  |  * | 
Organization |  |  | 
Technology |  |  | 
CPU time = Seconds = Instructions x Cycles x Seconds
Program Program Instruction Cycle
* Some instructions may of course take multiple cycles … see next slides for ACPI

## Slide 26: Average Cycles Per Instruction: processors with varying clocks per instruction
CPU time = CycleTime *  CPIi * Ii
i = 1
n
CPI =  CPIi * Fi where Fi = Ii
i = 1
n
Instruction Count
“Instruction Frequency” (Fi) (how often particular instruction is invoked)
CPI = Cycles / Instruction Count
  = (CPU Time * Clock Rate) / Instruction Count
Average Cycles Per Instruction (ACPI)
i.e. all instructions I1 to In
where CPIi is the cycles needed to complete instruction Ii

## Slide 27: Example: Calculating ACPI
Operation | Frequency (Fi) | CPIi | CPIi * Fi | Time %
Store | 10% | 2 | 0.2 | 13%
Load | 20% | 2 | 0.4 | 27%
Branch | 20% | 2 | 0.4 | 27%
ALU | 50% | 1 | 0.5 | 33%
ACPI | 100% |  | 1.5 | 100%

## Slide 28: Summarizing Performance
Arithmetic mean (weighted *arithmetic mean) tracks execution time (n = number runs):
  (Ti)/n or (Wi*Ti)
Harmonic mean (weighted harmonic mean) of rates (e.g., R = MFLOPS) tracks execution time:
  n/ (1/Ri) or n/ (Wi/Ri)
Normalized execution time useful for scaling performance
  e.g. X times faster than a Pentium4
  Arithmetic mean impacted by choice of reference machine (e.g. MIPS-1 processor)
Use the geometric mean for comparison:
  (Ti)^1/n
  Independent of chosen machine…
  but not good metric for total execution time
* Weighting assigns particular value (or priority of importance to certain runs)
Ti = time of run i

## Slide 29: Cost/Performance: The Relationship of Cost to Price?
Recurring Costs
  Component Costs
  Direct Costs, recurring costs: labor, purchasing, scrap, warranty
Non-Recurring Costs or Gross Margin
  R&D, equipment maintenance, machine and test equipment rentals, marketing, sales, financing cost, pretax profits, taxes, etc. etc.
Average Discount to get List Price
  Allowing for volume discounts and/or retailer markup

## Slide 30
Power concerns
(a GST* perspective)
* GST = General System Thinking

## Slide 31: GST – a brief aside
As good engineers it is appropriate to keep in mind socially conscious and environmentally friendly principles, to be aware of the potential implications of engineering work – which may have both good and bad consequences.
GST is a movement that was pioneered by the Australian Biologist Karl Bertalanffy in the 1930s
General Systems Theory (GST, or just Systems Theory nowadays) is a philosophy of thinking about systems that emphasizing ‘holism’ (complex wholes that cannot simply be partitioned to understand them) over ‘reductionism’ (which is the approach of separating into parts to understand the whole) – in terms of engineering (which much GST has been written about) the systems thinking approach is about considering the variety of systems that the system under development may influence or be influenced by.

## Slide 32: Computation Design Trends
Intel performance graph
For the past decades the means to increase computer performance has been focusing to a large extent on producing faster software processors.
This included packing more transistors into smaller spaces.
Moore’s law has been holding pretty well… when measured in terms of transistors (e.g., doubling number of transistors)
But this trend has drawbacks, and seems to be slowing…

## Slide 33: Power use
Power dissipation (hard not to have):
  Rate at which energy is taken from the supply (PSU) and transformed into heat
  P = E/t
Energy dissipation for a given instruction depends upon type of instruction (and state of the processor)
P = (1/CPU Time) *  E * I
i = 1
n
i
i

## Slide 34: Measures
MIPS/mW (also GIPS/mW or OPS/mW)
  Quantifying the amount of power dissipated per second for completing 106 instructions
This is becoming important to include in benchmarking results and product specifications to make comparisons more fair , e.g.
  for instance you might be comparing a machine that gives 100 MIPS to a machine that gives 80MIPS, but the first machine might use 2x the power of the second – is it still a fair comparison?

## Slide 35: Computation Design Trends – Power concerns
Slide 22 - Power over time.jpg
Processors are getting too power hungry! There’s too many transistors that need power.
Also, the size of transistors can't come down by much – it might not be possible to have transistors smaller than a few atoms! And how would you connect them up?
Now tending to multi-core processors.. Sure it can double the transistors every 2-3 years (and the power). But what of performance?
A dual core Intel system with GPU, LCD monitor
draws about 220 watts
Projections obviously we’ve seen the reality isn’t as bad

## Slide 36: The Energy-Flexibility Gap
Embedded Processors
SA110
0.4 MIPS/mW
ASIPs
DSPs
2 V DSP: 3 MOPS/mW
Dedicated
HW
Flexibility (Coverage)
Energy Efficiency
MOPS/mW (or MIPS/mW)
0.1
1
10
100
1000
Reconfigurable Processor/Logic
Pleiades
10-80 MOPS/mW
The usual, comfort-zone PC sits way down below the page… but is very flexible

## Slide 37: Cost of calculation
This is something that is becoming relevant considering the trend towards sharing computing infrastructure and cloud computing systems
  The developer doesn’t necessarily need to care what the underlying hardware costs, but rather what it will cost to do calculations on the available hardware.
There’s various ways to quantify this, let’s look at a basic view for now…
We look at cloud computing and commonly used cost models in more detail in a later lecture

## Slide 38
Calculation
per seconds per 1k$
Over time trend
Based on the cost of the underlying compute system (e.g. ENIAC for Vacuum tubes)

## Slide 39: Illustration of demand for computers (Intel perspective)
slide 22 - demand for computers.jpg
(unknown license)
Source:
alphabytesoup.files.wordpress.com/2012/07/computer-timeline.gif

## Slide 40: The Top500 List
The TOP500 list (www.top500.org) has provided a defining yardstick for supercomputing performance since 1993.
It is published 2x a year, it lists the world’s 500 largest installations and some of their main characteristics.
Systems are ranked according to their performance of the Linpack benchmark
  Linpack solves a dense system of linear equations.
Over time data collected for the list has enabled the early identification and quantification of many important technological and architectural trends related to high-performance computing.
Optional further reading: Strohmaier et al.“The TOP500 List and Progress in High-Performance Computing”, IEEE Compter. 2015 On Vula: L04 - 07328648 - The TOP500 List in HPC.pdf

## Slide 41
Image source: http://commons.wikimedia.org/wiki/File:Processor_families_in_TOP500_supercomputers.svg

## Slide 42
Image source: Strohmaier et al.“The TOP500 List and Progress in High-Performance Computing”, IEEE Compter. 2015
Supercomputer performance over time tracked by TOP500.
red and orange lines: performance of first and last systems
blue line: avg. performance of all systems.
Dashed lines: fitted exponential growth curves before and after 2008

## Slide 43
Almost the end of this lecture….
But a few reminders first!!!

## Slide 44: Seminar Groups
Try to start on formalizing groups
Group | Date | Members | Chapter
 | TERM1 | Microprocessor-based parallel systems | 
1 | 23 Mar 2017 | S. Winberg (done by lecturer) | The landscape of parallel computing research: a view from Berkeley
2 |  |  | CH1 A Retrospective on High Performance Embedded Computing and CH2Representative Example of a High Performance Embedded Computing System
3 |  |  | CH3 System Architecture of a Multiprocessor System
4 |  |  | CH5 Computational Characteristics of High Performance Embedded Algorithms and Applications (optional additional reading: CH15 Performance Metrics and Software Architecture)
5 |  |  | CH13 Computing Devices
 | TERM2 | FPGA / Reconfigurable parallel systems | 
6 |  |  | CH9 Application-Specific Integrated Circuits and CH10 Field Programmable Gate Arrays
7 |  |  | CH7 Analog-to-Digital Conversion
8 |  |  | CH14 Interconnection Fabrics
9 |  |  | CH24 Application and HPEC System Trends NOTE: this last seminar is on a Thursday as the Tues is a holiday
10 |  |  | CH20 Radar Applications (probably discard)
Use the Sign-up on Vula
to select your group

## Slide 45: What’s Next??
  Seminar #1
    The Landscape of Parallel Computing Research: A view from Berkeley

## Slide 46
Image sources:
Gold bar: Wikipedia (open commons)
IBM Blade (CC by 2.0) ref: http://www.flickr.com/photos/hongiiv/407481199/
Clipart, Takeaway, Clock, Factory and smoke – public domain CC0 (http://pixabay.com/)
Forrest of trees: Wikipedia (open commons)
Moore’s Law graph, processor families per supercomputer over years – all these creative commons, commons.wikimedia.org
Disclaimers and copyright/licensing details
I have tried to follow the correct practices concerning copyright and licensing of material, particularly image sources that have been used in this presentation. I have put much effort into trying to make this material open access so that it can be of benefit to others in their teaching and learning practice. Any mistakes or omissions with regards to these issues I will correct when notified. To the best of my understanding the material in these slides can be shared according to the Creative Commons “Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)” license, and that is why I selected that license to apply to this presentation (it’s not because I particulate want my slides referenced but more to acknowledge the sources and generosity of others who have provided free material such as the images I have used).