## Slide 1: WIISMA
Wide Instep Instruction Set Machine Architecture
A Multiple Instructions Single Data (MISD) system
EEE4084F
Lecture 09
EEE4084F
Presented by S. Winberg
Conceptual Assignment

## Slide 2
It’s quite clear to comprehend these more usual Flynn’s architectures
SISD
MIMD
SIMD
MISD
But the
is a rather weird one
Multiple instruction and single data (MISD), why would
one possibly ever want to use such a structure?...

## Slide 3: MISD
It turns out that there are some potential situations where the bizarre MSID structure could work
Remember that these processors will be doing different operations on the same data
This could be an effective processor structure for a stream processing system, where there is constantly new data being fed into the system that may need to be worked on simultaneously by multiple processing streams.
Data In
Seek start sequence#1
Decode Meth#1
Decode Meth#2
Seek start sequence#2
Analyse Payload
Analyse Payload
Example Application

## Slide 4: MISD
There is some flexibility of course in the architecture, in which each core could have its own (few) registers (making it a bit MD) but the processor limited to one core (Mcore) being able to read/write to memory/IO
  In effect only one core can perform a read/write to non register memory making it more SD that MD.

## Slide 5: The WIISMA
This is a very unusual processor design
The acronym summarizes its operation
  Wide Instep Instruction Set Machine Architecture =
  multiple long instructions
  all read in at once (i.e. instep)
MISD
  Can execute multiple instructions simultaneously
  But can only read/write one data item into or out of the processor to any one shared register (however, each core doesn’t need to use the same registers at a time)

## Slide 6: Purpose of conceptual assignment
The main purpose of this assignment is to get you
  thinking about a processor design,
  considering complications that may be encountered in the design of such a processor,
  applying problem-solving conceptual design problems to accommodate or work around certain architectural difficulties to provide needed functionality
  designing a sophisticated pipeline
  instruction set planning for a specialized processor / accelerator system

## Slide 7: What to do for this Project
Design of the system (mainly high level design)
  Refined block diagram
  Draft Schematic* (for a selection of components)
  Textual description
Instruction set planning
Discussion of benefits & drawbacks
A (simple) example assembly code program that the processor could execute (if actually implemented)
Theoretical performance analysis (estimating time to execute above example program)
Report to capture all of above
No implementation! 
* NB: in no way is the intention to do a schematic for the whole processor, only a particular part in order to examine the design and potential solution strategies more deeply

## Slide 8
Architecture overview of WISSMA

## Slide 9: (Desired) Approach: A discussion point to stimulate the mind
Simulating the design (on paper or a whiteboard) and brainstorming aspect of the system/solutions are what computer engineers often use to share and discuss ideas which helps to establish good designs and concept plans.

## Slide 10: Only part of an initial dev. cycle
Requirements
Modeling
Design &
HDL Coding
Trace & Route
/ Compile
Test Model
(e.g. MATLAB simulation)
Deploy / put in environment
Timing Accurate Simulation /
Test on H/W
System Test
Bypassing

## Slide 11: Have some considerations for the development cycle for the system
Provide some reflection (essay style) on potential risks that may occur in this project (were it done for real); discuss in intro.

## Slide 12
How does WIISMA work?

## Slide 13
Component | Description
Acore | Arithmetic core
Ccore | Control core
Mcore | Memory core
Icache | Instruction cache
Regs | Registers shared between cores
Dual Port DRAM | Random access memory accessible by Mcore and Icache.
WIISMA processor has a number of components responsible for certain tasks.
The components and their descriptions are listed below.

## Slide 14: How does WIISMA it work?
The WIISMA has
  A number of ACores : arithmetic core
  One CCore : control core
  One MCore : Memory controller
ACore : does arithmetic operations (+,-,*,<,>,=,etc)
CCore : controls execution, jump to address, etc.
MCore : accesses off chip memory and contains memory cache for processor

## Slide 15: How does WIISMA it work?
The Icache reads in instructions from the Dual Port RAM, from address IP
The Icache simply (blindly) reads in instructions from memory continuously
When a complete instruction is loaded, parts of the instruction are sent to each Acore and to the Ccore
If there are n Acores, then the processor runs (n+1) operations in parallel
There are a selection of shared registers, SA,SB, etc, and MP and MD (mem pointer and mem data) that are accessible to all cores.
Each core (except MCore) has private registers R1..R4
Only the CCore can instruct the MCore to do a read/write of one word (i.e. MD) to main memory (at mem[MP])

## Slide 16: How does WIISMA it work?
Only the CCore can instruct the ICore to change its IP or flush its instruction queue (i.e. the instructions that it has read in from memory but not yet processed)
The ACores need to be kept busy
The MCore reads/write memory
  Read: MD = mem[MP]
  Write: mem[MP] = MD
All the instructions start at the same time
The Icore continues loading instructions while the Acores are busy processing
Icore only loads new instructions into the other cores once all the cores are complete

## Slide 17
W-Instructions
WIISMA wide instruction configuration
Acore1 Instruction
Acore1 Constant
Acore2 Instruction
Acore2 Constant
…
Ccore Instruction
Ccore Constant

## Slide 18
CCore Instruction | Description
NOP | No OPeration. Does nothing.
B <reg> | Branch to the address help by register <reg>
BR <const> | Branch relative a constant value i.e. does B IP+const
BGT <ref>, BGE <reg> etc. | Conditional branch if greater-than flag set, Conditional branch if greater-than and equal flags are set. (See description for B <reg>).
BRGT <ref>, BRGE <reg> etc. | Conditional relative branching. (see BGT above).
EX <reg1>, <reg2> | Swaps value between registers, works on R-registers and shared S-registers; cannot be used with IP or MD.
LDR <reg>,<const> | Loads a constant value into a register (all except MD; to generate an exception a command such as LDR IP,0 can be used).
LDR <reg1>, [<reg2>] | Loads value from memory address stored by reg2 into reg1. Note that MI, MD and reg1 both change after this instruction is executed.
LDR <reg1>, [<reg2> + <const>] | Loads value from memory address (reg2 + const) into reg1. Const is an offset. Note that MI, MD and reg1 both change after this instruction is executed.
STY | Stay command. Supress the Mcore from reading the next word from memory.
W-Instructions: Ccore

## Slide 19
W-Instructions: Acore
ACore Instruction | Description
NOP | No OPeration.
ADD <reg1>, <reg2>, <reg3> | Do add operation, i.e. reg3 = reg1 + reg2. The MD instruction can only be read, it cannot be written to.
MUL <reg1>, <reg2>, <reg3> | Do multiply operation, i.e. reg3 = reg1 * reg2. The MD instruction can only be read, it cannot be written to.
EX <reg1>, <reg2> | Exchange two registers. Neither register can be MD.
LDR <reg1>, <const> | Load a constant value into reg1 (cannot be MD register). Writing to the MI register from one of the Ccores effectively changes the memory address to be read into MD in two instructions time (since the MD value for the next instruction would have already be read but not yet copied over to the MD register, which would happen after all instructions are complete and before the next set of instructions are executed).
STY | Stay command. Supress the Mcore from reading the next word from memory.

## Slide 20
How WIISMA executes programs

## Slide 21: Example WIISMA program
Consider the C code:
/* assume that the variables maxv = 10 and minv= 0 have already been assigned respectively to internal register A in core 2 and internal register B in core 3; */
int sc = ptr[i] * sa;
sb = 100;
if (ptr[i] > maxv || ptr[i] < minv) sc = mini;
i++;

## Slide 22: WIISMA example program
Considering the previous code, the first instruction for the WISSMA might look like this:
Acore instructions Ccore instructions
Acore1 Acore2 Acore3 Ccore
MUL SA, MD, SC CMP MD, A CMP MD, B LDR SB, #100
(ptr[i] * sa)
where MD == ptr[i]
ptr[i] > maxv
ptr[i] < minv
sb = 100;

## Slide 23: Instruction set planning
Acore instructions
  Acore1 Acore2 Acore3
  MUL SA, MD , SC | CMP MD, A | CMP MD, B
Ccore instructions
  LDR SA, [SB]
Imagine all the above instructions executing at once. Only the Ccore can change the memory address to read, or write to memory, or do jumps
Clearly would need a specialized compiler

## Slide 24: Execution time calculation
Time to load in the instructions (for case using cache, for case without cache)
Time before first instruction starts executing
Time to execute the set of instructions
  Which one finishes last?
Any time needed to finalize operations before starting next instruction?
Adding it all up to get best case and worst case execution times

## Slide 25: Procedure
Read the assignment (on Vula)
Choose a teammate
Discuss and strategize the problem
Divide up tasks and do them
Report due 12 May 2017

## Slide 26: Marking
EEE4084F Digital Systems |  |  | 
Conceptual Assignment |  |  | 
Fill in group#, STDNUM and mark allocations in the unshaded columns. Shaded columns are automatically filled in. |  | Group# | 
Criteria | Max | STDNUM001 | STDNUM002
Cover Page | 5 |  | 0
Preamble Abstract. Table of contents. | 5 |  | 0
Introduction (Sect. 1) Outlines the system and should also include a brief summary of major design decisions. Discussion of development process. | 10 |  | 0
Processor Design (Sect. 2) Including use of images. | 20 |  | 0
Instruction Set (Sect. 3) Marks awarded based on how well instructions are presented, structured and described. | 20 |  | 0
Programming (Sect. 4) | 10 |  | 0
Discussion & Conclusion (Sect. 5) | 10 |  | 0
Creativity / innovative solutions. This criterion is used to award good design ideas. | 10 |  | 0
Style and professionalism. Including page numbers, headings, language, references. | 10 |  | 0
Total: | 100 | 0 | 0