## Slide 1
Lecture 18
FPGA Interns & Performance Comparison
Lecturer:
Simon Winberg
Digital Systems
EEE4084F
Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)

## Slide 2: Lecture Overview
FPGA Interns
FPGA vs CPU performance

## Slide 3: Structure of FPGA
A completely different architecture for PLAs was introduced in the mid-1980’s that uses RAM-based lookup tables instead of AND-OR gates to implement combinational logic
These devices are called field programmable gate arrays (FPGAs).
The device consists of an array of configurable logic blocks (CLBs) surrounded by an array of I/O blocks
FPGAs really don’t have AND and OR gates, (they have a few) but rather just RAM look-up tables.

## Slide 4: FPGA Interns
EEE4084F
Skip to slide 22; already covered in text book but scan through these slides to ensure you are well versed in these issues.

## Slide 5: FPGA internal structure
Image adapted from Maxfield (2004)
Programmable logic element (PLE) (or FPLE*)
* FPLE = Field Programmable Logic Element
Note: one programmable logic block (PLB) may contain a complex arrangement of programmable logic elements (PLE).
The size of a FPGA or programmable logic device (PLD) is measured in the number of LEs (i.e., Logic Elements) that it has.

## Slide 6: Logic Elements – Remember your logic primitives
You already know all your logic primitives…
  The primitive logic gates
    AND, OR, NOR, NOT, NOR, NAND, XOR
    AND3, OR4, etc (for multiple inputs).
  Pins / sources / terminators
    Ground, VCC
    Input, output
  Storage elements
    JK Flip Flops
    Latches
  Others items: delay, mux
OR
Input Pin
Output Pin
Altera Quartus II representations

## Slide 7: Look Up Tables (LUTs)
A simple but powerful approach to FPGA design is to use lookup tables for the PLBs. These are usually implemented as a combination of a multiplexer and memory (even just using NOR gates)
Essentially, this approach is building complex circuits using truth tables (where each LUT enumerates a truth table)
The usual strategy for implementing PLBs
examples follows…

## Slide 8: Simple 3-LUT implementation for a PLB
0
1
1
0
1
0
0
1
8-bit static memory
3
3-bit input bus
1-bit output
000
001
010
011
100
101
110
111
Any guesses as to what logic circuit this LUT implements?
input values

## Slide 9: Simple 3-LUT implementation for a PLB
input lines
It’s an XOR of the 3 input lines!!!
output
0
1
1
0
1
0
0
1
000
001
010
011
100
101
110
111
in out

## Slide 10: Mainstream* Programmable Logic Block (PLB)
k-input LUT
DFF
clock
…
k inputs
output
config_sync
Configure synchronous or asynchronous response (i.e. a line from another big LUT).
0
1
Image adapted from Maxfield (2004)
Another example for implementing an alternate logic function.
* Used by manufacturers like Xilinx

## Slide 11: Logic block clusters (LBCs) and Configurable logic blocks (CLBs)
Assume a k-input LUT for each logic block (LB)
Assume N x LBs per logic cluster
BLEs in each logic clusters are fully connected or mostly connected
Diagram adapted from Sherief Reda (2007), EN2911X Lecture 2 Fall07, Brown University
The diagram shows the same input lines (I) are sent to each LB, in addition to each of the N LBs’ output lines. Each LB operates on 4 input lines at a time, and a MUX is used to decide which input to sample. The MUXs may be configured from a separate LUT, or could be controlled by the LB it is connected to.
LB
LB
…
N x LBs

## Slide 12: Xilinx L and M Slices Approach for configurable logic blocks (CLBs)
“Every slice contains four logic-function generators (or LUTs), eight storage elements, wide-function multiplexers, and carry logic. These elements are used by all slices to provide logic, arithmetic, and ROM functions. In addition to this, some slices support
two additional functions: storing data using distributed RAM and shifting data with 32-bit registers. Slices that support these additional functions are called SLICEM; others are called SLICEL. SLICEM represents a superset of elements and connections found in all slices. Each CLB can contain zero or one SLICEM. Every other CLB column contains a SLICEMs.
In addition, the two CLB columns to the left of the DSP48E columns both contain a SLICEL
and a SLICEM.”
Source: http://www.xilinx.com/support/documentation/user_guides/ug364.pdf pg 8

## Slide 13
SLICEM slices support additional functions; they are a superset of SLICELs; i.e. the have all the standard LEs plus some additions.
Source: http://www.xilinx.com/support/documentation/user_guides/ug364.pdf pg 9

## Slide 14
SLICEL slices contain the standard set of LEs for the particular FPGA concerned. As the diagram shows, it looks a little less complicated than the design of a SLICEM.
Source: http://www.xilinx.com/support/documentation/user_guides/ug364.pdf pg 10

## Slide 15: Evaluating Performance
Evaluating synthesis (simplified) of an FPGA design

## Slide 16: HDL to FPGA execution & LE cost
Map ‘AND(e,f,g)’ to LB1
In order to implement a HDL design, the design need to be decomposed and mapped to the physical LBs on the FPGA and the interconnects need to be appropriately configured.
Example:
x = AND(e,f,g)
y = AND(b,NAND(NAND(b,c),d))
out = NAND((NAND(x,y),NAND(a,y))
out
x
y
Map ‘NAND((NAND(x,y),NAND(a,y))’ to LB2
Map ‘AND(b,NAND(NAND(b,c),d)) ’ to LB3
Costing: 3 LBs, 8 LEs (assuming LBs have LEs that are AND or NAND gates)

## Slide 17: Timing calculations
The previous slide didn’t show whether the connections were synchronized (i.e., a shared clock) or asynchronous –since they are all logic gates and no clocks show it’s probably asynchronous
Determining the timing constrains for synchronous configurations are generally easier, because everything is related to the clock speed. Still, you need to keep in mind cascading calculations.
For asynchronous use, the implementation could run faster, but can also become a more complicated design, and be more difficult to work out the timing…

## Slide 18: Async Timing calculations
Keep in mind that the propagation delays for the various gates / LUTs may be different – for example, in the previous example, let’s assume each AND may take 6ns to stabilise, and the NANDS 10ns.
So time to compute out is =
  MAX OF (time to compute x, time to compute y) + 2x10ns = (2x10ns+6ns) + 20ns = 46ns = pretty fast!! Or is it??
  Compared to a 1GHz CPU using just registers (and no mem access)?
  Try this calculation for yourself ...
  (assume each instruction takes on avg. 3 clocks due to pipeline, data dependencies, etc, as worst case performance on a RISC processor)

## Slide 19: Comparing to CPU speed
CPU running at 1GHz  each clock 1ns period
Assume each instruction takes ~ 5 clocks each due to pipeline etc
CODE:
int doit ( unsigned a, b, c, d, e, f, g ) {
unsigned x = AND(e,f,g);
unsigned y = AND(b,NAND(NAND(b,c),d))
out = NAND((NAND(x,y),NAND(a,y))
return out;
}
unsigned t1 = AND(e,f);  1 instruction, i.e. AND t1,e,f
unsigned x = AND(t1,g);
unsigned t1 = NAND(b,c)
unsigned t2 = NAND(t1,d)
unsigned y = AND(b,t2)
t1 = NAND(x,y)
t2 = NAND(a,y)
out = NAND(t1,t2)
in all 8 instructions  8 x 3 clocks ea.
= 24 ns (assuming all registers pre-loaded)
A speed-up of 1.92 over the FPGA case
But some of these
Can’t be done as just 1
RISC instruction.

## Slide 20: Digital Clock Manager (DCM) blocks
An important element included in FPGA designs nowadays are DCM blocks, which are used to eliminate clock distribution delay and can also increase or decrease the frequency of the clock

## Slide 21
Image sources:
man working on laptop – flickr
scroll, video reel – Pixabay http://pixabay.com/ (public domain)
Disclaimers and copyright/licensing details
I have tried to follow the correct practices concerning copyright and licensing of material, particularly image sources that have been used in this presentation. I have put much effort into trying to make this material open access so that it can be of benefit to others in their teaching and learning practice. Any mistakes or omissions with regards to these issues I will correct when notified. To the best of my understanding the material in these slides can be shared according to the Creative Commons “Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)” license, and that is why I selected that license to apply to this presentation (it’s not because I particularly want my slides referenced but more to acknowledge the sources and generosity of others who have provided free material such as the images I have used).
References: Verilog code adapted from http://www.asic-world.com/examples/verilog