## Slide 1
Lecture 20
More Verilog, Statements, Constraints
Lecturer:
Simon Winberg
Digital Systems
EEE4084F
module myveriloglecture ( wishes_in, techniques_out );
…
// implementation of today’s lecture
…
endmodule
Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)
statemachine

## Slide 2: Lecture Overview
Brief recap
Busses and endianess
Functions in Verilog
Implementing state machines
Constraints
UCF Files

## Slide 3: Module declaration (recap)
Modules are defined in Verilog as follows:
module mymodule (a, b, x, y);
input a, b; // these are inputs, usually first
output x, y; // this an output, listed usually after inputs
x <= or(a,b); // these all executed at same time
y <= and(a,b);
endmodule // no semicolon needed after endmodule

## Slide 4: Initial block
The initial block is like a constructor for a Verilog module in simulation. It is activated the first time the module starts up.
Used in simulation to set up conditions and to implement test benches.
module testbench; // top level module
wire a, b, x; // set up some signals
add myadd(a,b,x); // module to test
myAnd_tb1 tb(a, b, x); // use this test
endmodule;
module myAnd_tb1(a,b,x);
input a,b;
output x;
reg a, b; // registered inputs
initial begin
// log these signals as follows:
$monitor ($time,
“a=%b, b=%b, x=%b”, a, b, x);
// exercise the signals
a = 0; b = 0;
#10 b = 1;
#10 a = 1;
#10 b = 0;
#10 $finish; // tell simulator to quit
end // end initial
endmodule

## Slide 5: Monitor : a standard Verilog simulation operation
The monitor operation is sensitive to a selection of signals. Whenever one of the signals change, it prints out whatever is requested to be printed, using a printf type formatting
$monitor(text,signals) — give it a string (or multiple strings) followed by a list of variables.
e.g. $monitor(“mysigs: ”, “a=%b b=%b:”, a,b);
Examples:
$monitor($time,”a=%b”,a); // displays time value followed by a=xx (bin val)
// $time is actually a string value

## Slide 6: The always@ (sensitivity_list)
The always@ expression is used within a Verilog module to group operations that activate whenever the sensitivity list is triggered
Syntax:
always @ (<sensitivity1, sensitivity2, …>)
begin
<actions>
end
Example: Implementing a D-type flip-flop …
Used in behaviour descriptions and statemachines

## Slide 7: always@ Example : D-type Flip Flop
module flipflop (din, clk, rst,q);
input din, clk, rst;
output q;
reg q; // q is a registered output
always @ (posedge clk) // whenever clk
begin
if (rst == 1) q = 0; // keep q low in reset
else q = din;
end
endmodule

## Slide 8: Busses & endian
Busses or bit signal vectors are specified as follows:
  reg [20:0] data; // little endian LSB in bit 0
  reg [0:20] data; // big endian MSB in bit 0
It doesn’t really matter if you are using them just as busses, it is only relevant when applying operations such as add.

## Slide 9: Functions in Verilog
Functions can be used as macros within the body of a Verilog module. These can effectively save typing. They work differently to module instantiations. These are defined in a module.
Can only have input parameters
Example:
function [31:0] negate; input [31:0] a; negate = ~a; endfunction
reg [15:0] a;
wire [15:0] x;
assign b = negate (a); initial begin a=10;
a = add(1, a); $display(" a=%b -a=%b”, a, b); end
functions are not modules in Verilog

## Slide 10: Example function: Converting endianness
If need be you can construct a function to convert endianness, e.g.:
  function [31:0] toBigEndian;
  // transform data from little-endian to big-endian
  input [31:0] x;
  toBigEndian = {x[7:0], x[15:8], x[23:16], x[31:24]};
  endfunction

## Slide 11: Vectors & Signal concatenation { }
module adder4 (a, b, cin, sum, cout);
input [3:0] a, b; // 2x 4 bit vector inputs
input cin; // carry input
output [3:0] sum; // 4-bit little endian vector
output cout; // carry out
// perform the adder operation
assign {cout,sum} = a + b + cin;
// the leftmost is MSB since it is little endian
endmodule
Syntax for concatenating wires: { x1, x2, … xn } the collective can be used just the same as any other variable.

## Slide 12: Blocking/Non-blocking statemets
Blocking
module blockFFs (
input D, input clk,
output reg Q1, output reg Q2)
always @ (posedge clk)
begin
Q1 = D;
Q2 = Q1;
end
endmodule
Non-blocking
module nonblockFFs (
input D, input clk,
output reg Q1, output reg Q2)
always @ (posedge clk)
begin
Q1 <= D;
Q2 <= Q1;
end
endmodule

## Slide 13: Implementing a FSM
Creating finite state machines in Verilog

## Slide 14: Statemachines
A state machine has:
  Input events
  Output events
  Set of states
  A function that maps (state,input)  (state,output)
  A indication of the initial state
A Finite State Machine (FSM) has a limited number of states

## Slide 15: Implementing a FSM with Verilog
The state machine needs a register to store its state
It is sensitive to zero or more inputs, which can change state and/or produce an output

## Slide 16: The state register
States could be numbered in sequence 0 .. 2n-1 where n is the number of bits for the state.
Or a different encoding / ordering scheme could be used to make state changes more robust, e.g.:
  use of grey scale or ‘one hot’ encoding (where ‘one hot’ means there is just one pin in the state set at a time)

## Slide 17: The states and state changes
Need a means to force initial state at startup (i.e. reset state register)
  Typically a reset handler does this.
Specifying and changing states
  Usually a case construct is used to define the states, but could use ifs and elses
Need to decide if the statemachine
  is synchronous (clocked) or
  asynchronous (activates whenever an input changes)
May need recovery mechanism (e.g. watchdog or recovery default state)

## Slide 18: Example Statemachine
WAIT
ack=0
PING
ping
ACKNack=1
~ping
ping
ack
clk
AliveFSM
Sends blip out ack if pinged
Notes: Must only send ack only after ping goes low
// Code your design here
module alivefms (input clk, input reset, input ping, output reg ack,
output reg[1:0] state);
parameter [1:0] WAIT = 2'b11;
parameter [1:0] PING = 2'b01;
parameter [1:0] ACKN = 2'b10;
always @(posedge clk or posedge reset or
posedge ping or negedge ping)
begin
if (reset)
begin
state <= WAIT;
ack <= 0;
end else
begin
case(state)
WAIT: begin
if (ping) state <= PING;
else state <= WAIT;
ack <= 0;
end
PING: if (ping) state <= PING;
else state <= ACKN;
ACKN: begin
ack <= 1;
state <= WAIT;
end
default: state <= WAIT;
endcase
end
end
endmodule
…
 Start up
 Activation
 States
 Recovery

## Slide 19: Create a testbench
// testbench for alivefsm
module alivefms_tb ();
reg clk, reset, poke;
wire ack;
wire [1:0] state;
integer i;
// instantiate the FSM
alivefms alivefsm_tb (clk,reset,poke,ack,state);
initial // method for testing the FSM:
begin
// enable monitoring of wires of interest
$monitor("reset=%d state=%d poke=%d ack=%d\n",
reset,state,poke,ack);
clk = 0; reset = 1; #5 // do the reset
reset = 0; clk=0; #5
poke = 1; clk=1; #5 // poke the fsm
poke = 0; #5 // release poke
clk = 0; #5 // needs a clk transition
clk = 1; #5
if (ack == 1) // check if worked as planned
begin
$display("SUCCESS\n");
end
end
endmodule
Avail onlne at: https://www.edaplayground.com/x/25N5

## Slide 20: Run on iverilog (or other sim)
$ iverilog '-Wall' design.sv testbench.sv && unbuffer vvp a.out reset=1 state=3 poke=x ack=0 reset=0 state=3 poke=x ack=0 reset=0 state=1 poke=1 ack=0 reset=0 state=2 poke=0 ack=0 reset=0 state=3 poke=0 ack=1 SUCCESS Done

## Slide 21: Attributes and Constraints
A Xilinx Perspective

## Slide 22: Difference between Attributes and Constraints
Two types of attributes:
  Predefined attributes (a part of the 1076 standard*)
  Those outside the standard provided by the designer or by the design tool supplier (such as Xilinx or Altera)
* http://vhdl-manual.narod.ru/books/ieee_manual.pdf

## Slide 23: Classes of FPGA constraints
Grouping Constraints
Timing Constraints
Logical Constraints
Physical Constraints
Mapping Directives
Placement Constraints
Routing Directives
Synthesis Constraints
Configuration Constraints
Source: http://xilinx.eetrend.com/files-eetrend-xilinx/forum/201103/1746-3205-02a_ucf_editing_12.pdf

## Slide 24: Where constrains can be defined
Depending on a attribute they can be defined in various places:
  Constraints Editor for Timing Constraints
  Floorplanner for Non-timing placement constraints
  PACE for IO placement and area constraints
  Floorplan Editor for IO placement and area constraints
  Schematic and Symbol Editors for IO placement and RLOC constraints
The UCF (User Constrains File) is where you can manually (and quickly!!) define constraints, we will focus on this option.

## Slide 25: UCF
Xilinx User Constraints Files

## Slide 26: UCF Files
UCF files are in ASCII
They are used to specify constraints on the logical design
You can use your favorite text editor to edit them UCF (can edit in ISE)
NCF file:
  this often goes with UCT file.
  The Netlist Constraint File (NCF) is also an ASCII file that is usually generated by some synthesis programs

## Slide 27: UCF Files Syntax
UCF files are generally case sensitive
However any Xilinx constraint keyword (e.g., LOC, PERIOD, LOW, HIGH) may be entered in all uppercase, in all lower-case, or mixed case.
Each statement is terminated by a semicolon (;) - the errors are sometimes cryptic, not obviously indicating missing the ‘;’.
Keep a blank line at the end of the file
Comments are started with # and end at the end of the line. The C / C++ comments // and /**/ are also supported

## Slide 28: UCF Files Syntax
Each line have a structure such as:
  {NET|INST|PIN} “name” constraint;
Particular bus lines on a bus are indicated by using name<n> where n is the bit (counted from 0) that you want to refer to
Typical usage: setting location of pins
  NET reset LOC=P16;
  NET leds<0> LOC=P23;
  NET leds<1> LOC=P24;

## Slide 29: UCF quick features
Wildcards can be used for the naming, such as
  The asterisk (*): represents any string of zero or more characters
  The question mark (?): represents a single character
Examples:
  NET “leds*” SLOW;
  NET “CLK?” FAST;

## Slide 30: Xilinx Constraints Editor
The Xilinx Constraints Editor is useful for enter timing constraints
The GUI simplifies constraint entry by using wizards to guide the user through constraint creation, without needing to understand UCF file syntax.
Although it is useful to see what kinds of constrains result in the file as this could help speed up constrains entry/reuse in future projects

## Slide 31: Constraints Editor
Runs synthesize etc.
Provides functions to find pins, to assign wires to groups, to structure clock domains.
Can view the UCF file lines in the “UCF Constraints” tab (this includes the comment lines).

## Slide 32: PERIOD constraints
The PERIOD constraint provide accurate timing requirements, so it indicates…
  Clock skew between the source and destination registers / flip-flops
  Synchronous elements clocked on edge
  Unequal clock duty cycles
  Clock jitter
ISE uses this information to place and route elements of your design in an attempt to satisfy these requirements (and thus make the design work on hardware)

## Slide 33: Example PERIOD constraint
Assumptions…
  50% duty cycle on CLK line
  PERIOD constraint of 10 ns
Clocking
  Because reg2 will be clocked on the falling edge of CLK, the link between the flip-flops will be constrained to 50% of 10 ns = 5 ns
The implementation tools will automatically account for triggering the one flip-flop on the rising edge and another on the falling edge
BUFG
INV
CLK
FF1
FF2
The PERIOD statement covers all timing paths that start or end at a register, latch, or synchronous RAM that are clocked by the reference net
NET clock PERIOD = 10ns ;

## Slide 34: Tutorial on using UCF files
Recommended tutorial by Xilinx on understanding and using UCF files
  http://xilinx.eetrend.com/files-eetrend-xilinx/forum/201103/1746-3205-02a_ucf_editing_12.pdf
Exam hint: statemachines are highly likely to come up in the exam or class test, building statemachines is an essential skill for HDL developers.

## Slide 35
Image sources:
man working on laptop – flickr
scroll, video reel, big question mark – Pixabay http://pixabay.com/ (public domain)
Disclaimers and copyright/licensing details
I have tried to follow the correct practices concerning copyright and licensing of material, particularly image sources that have been used in this presentation. I have put much effort into trying to make this material open access so that it can be of benefit to others in their teaching and learning practice. Any mistakes or omissions with regards to these issues I will correct when notified. To the best of my understanding the material in these slides can be shared according to the Creative Commons “Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)” license, and that is why I selected that license to apply to this presentation (it’s not because I particularly want my slides referenced but more to acknowledge the sources and generosity of others who have provided free material such as the images I have used).
References: Verilog code adapted from http://www.asic-world.com/examples/verilog