## Slide 1
Lecture 5:
Benchmarking cont., parallel programming models, Aspinall structures, data dependencies, shared memory partitioning
Lecturer:
Simon Winberg
Digital Systems
EEE4084F
Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)
mutex

## Slide 2: Lecture Overview
Performance benchmarking consideration
Timing in C
C Example using precision timing
HDL example to contemplate
Parallel Programming Models
Parallel System Approaches
Data vs. Task Parallel
Types of Data Dependences
Using a mutex
Shared memory partitioning approaches

## Slide 3: Benchmarking tips
Timing methods have generally been included in baseline projects for the pracs (e.g. tic and toc for OCTAVE/MATLAB)
Avoid having many programs when doing performance benchmarking as this may interfere slightly with timing results. Running tests on virtual machines can also have inconsistencies.

## Slide 4: Last resort… counting instructions
int ary[1024];
int i, j = 0;
for (i=0; i<1024, i++) j += i*ary[i];
If you’re really out of execution timing facilities, or even a simulator that can give good estimates, then you could resort to manually calculating the execution performance based on the assembly code, and in particularly the instructions, that would be executed. This is of course more appropriate for hypothetical cpu designs where there is no real hardware or even a simulator on which to test the performance.
; dissessembled code
movl $0x0,0x18(%esp)
movl $0x1,0x14(%esp)
movl $0x0,0x1c(%esp)
jmp 0x40136d <main+57>
mov 0x1c(%esp),%eax
imul 0x14(%esp),%eax
add %eax,0x18(%esp)
incl 0x1c(%esp)
cmpl $0x3ff,0x1c(%esp)
jle 0x40135c <main+40>
mov 0x18(%esp),%eax
mov %eax,0x4(%esp)
movl $0x403024,(%esp)
call 0x401bc0 <printf>
mov $0x0,%eax
ret

## Slide 5: Class activity / take-home assignment
Matrix operations are commonly used to demonstrate and teach parallel coding
The scalar product (or dot product) and Matrix multiply are the ‘usual suspects’
Vector scalar product
Matrix multiplication
Both of these operations can be successfully
Implemented as deeply parallel solutions.
Ci,j =  Ai,k Bk,j
k

## Slide 6: Class activity / take-home assignment
Attempt a pseudo code solution for parallelizing both the:
  Scalar vector product algorithm and the
  Matrix multiplication algorithm
Assume you would want to implement your solution in C or C++ (i.e. your pseudo code should follow C-type operations)
Next consider how you would do it in hardware on a FPGA (draw flowchart / schematic)
If time is too limited, just try the scalar product. If you have more time, and are
real keen, the by all means experiment with writing and testing real code to see
that your suggested solution is valid.

## Slide 7: Suggested function prototypes
  void matrix_multiply (float** A, float** B, float** C, int n)
  {
  // A,B = input matrices of size n x n floats
  // C = output matrix of size n x n floats
  }
Matrix multiply:
Scalar product:
  float scalarprod (float* a, float* b, int n)
  {
  // a,b = input vectors of length n
  // Function returns the scalar product
  }

## Slide 8: Scalarprod.cpp – golden measure
float scalarprod (float* a, float* b, int n) {
unsigned i;
CPU_tic(); // get initial tick value
// Do processing ...
srand((unsigned int)time(NULL)); // provide random seed
// first initialize the vectors
for (i=0; i<n; i++) {
a[i] = random_f();
b[i] = random_f();
}
float sum = 0.0f;
for (i=0; i<n; i++) {
sum = sum + (a[i] * b[i]);
}
// get the time elapsed
double t1 = CPU_toc(); // get final tick value
std::cout << "scalarprod " << " took " << t1 << " ms\n";
}
An example Golden measure / sequence solution
Lets have a look at two of the functions that aren’t available in stdlib or iostream …

## Slide 9: Scalarprod.cpp – functions needed
// random_f returns a random value between 0.0 and 1.0
float random_f ()
{
return (float)rand()/(float)(RAND_MAX);
}

## Slide 10: Scalarprod.cpp – CPU_tic and CPU_toc
#include <windows.h>
#include <ctime>
LARGE_INTEGER clk_frequency, clk_tic;
void CPU_tic () {
QueryPerformanceFrequency(&clk_frequency);
QueryPerformanceCounter(&clk_tic);
}
double CPU_toc () {
LARGE_INTEGER clk_toc;
QueryPerformanceCounter(&clk_toc);
return (double)(clk_toc.QuadPart - clk_tic.QuadPart) * 1000.0 / clk_frequency.QuadPart;
}
double CPU_ticks_to_ms (long ticks) {
return (double)ticks / CLOCKS_PER_SEC * 1000.0;
}
Should have this all in a separate module
(Windows version)

## Slide 11: Scalarprod.cpp – CPU_tic and CPU_toc
#include <iostream>
#include <ctime>
#include <sys/time.h>
#include <stdlib.h> // for srand, rand
timeval clk_tic, clk_toc; // store the timestamps
void CPU_tic () {
gettimeofday(&clk_tic, NULL);
}
double CPU_toc () {
gettimeofday(&clk_toc, NULL);
double t = double(clk_toc.tv_sec -clk_tic.tv_sec )
+ double(clk_toc.tv_usec-clk_tic.tv_usec)*1.e-6;
return t;
}
double CPU_ticks_to_ms (long ticks) {
return ticks * 1000.0;
}
Linux version (probably poor accuracy if you try running on Windows, e.g. compiling using DevC++)

## Slide 12: Scalar product – parallel version?
If we consider implementing a CPU version using e.g. pthreads, we need to think about a balance between the cost of spawning and joining threads and the time each thread spends.
So the most parallel approach of each thread of working on only one element from each vector, doing one multiply, will likely give poor performance because the time to spawn all the threads may be longer than the time to do the multiply and add. Especially considering that a mutex is probably needed for the add.

## Slide 13: Scalar product – parallel version?
We would rather compromise, balance the workload better so that each thread works on multiple elements of each vector.
So the approach would be:
  Assuming N length vectors, M threads, then: each thread works on N/M elements, multiplies and keeps a local sum, then at the end of the operation needs to add to a shared sum value (which would need to be protected by a mutex).
Some example code follows…

## Slide 14: Scalarprod.cpp – parallel version
#include <iostream>
#include <pthreads> .. Others libs ...
// First plan data to share between threads:
// Define data structure to be shared between the threads
struct DotprodData {
double *A;
double *B;
double sum;
unsigned block_len;
} ;
// Allocate the shared data, thread process data, and a mutex
DotprodData shared_data; // data that is shared
pthread_t thread[N_THREADS]; // thread data
pthread_mutex_t mux_sum; // mutex for summing up the results

## Slide 15: Scalarprod.cpp – parallel version
/** Thread operation, multiplied and adds one block of the shared vectors */
void *dotprod(void *arg) {
/* Define and use local variables for convenience */
long i, m, start, stop;
double my_sum, *A, *B;
long offset = (long)arg;
// read in to local registers
m = shared_data.block_len;
start = offset*m;
stop = start+m;
// set up arrays
A = shared_data.A;
B = shared_data.B;
// do the calculation
my_sum = 0;
for (i=start; i<stop; i++) {
my_sum = my_sum + (A[i] * B[i]);
}
/* Lock mutex prior changuing the shared data. */
pthread_mutex_lock (&mux_sum);
/* This code is protected by the mutex mux_sum */
shared_data.sum += my_sum;
// debug info to print what this thread has done
printf("thread#%lu computed %lu -> %lu: my_sum=%f " "total_sum=%f\n",offset,start,stop,my_sum,shared_data.sum);
pthread_mutex_unlock (&mux_sum); /* release the mutex */
/* Exit the thread */
pthread_exit(0);
}
PLAN WHAT THE THREAD PROCESS WILL DO…
But need to first calculate what
part of the vectors to work on

## Slide 16: Scalarprod.cpp – parallel version
int main (int argc, char *argv[])
{
… some vars initialized left out here …
… initialize the vectors …
/* set the sum to 0, note that the sum will be locked by a mutex */
shared_data.sum=0.0;
/* initialize the mutex for protecting the shared sum variable */
pthread_mutex_init(&mux_sum, NULL);
/* Initialize the threads library */
pthread_attr_init(&attr);
pthread_attr_setdetachstate(&attr, PTHREAD_CREATE_JOINABLE);
/* start the timer: */
CPU_tic();
/* spawn the threads */
for (i=0;i<N_THREADS;i++)
pthread_create(&thread[i], &attr, dotprod, (void *)i);
…
/* This main thread now just waits on the other threads to complete. */
for (i=0;i<N_THREADS;i++) pthread_join(thread[i], &pstatus);
/* At this point the joins are all complete, i.e. the threads have completed. */
double t1 = CPU_toc(); /* End the timer */
/* Display the results of the vector product... */
printf ("Sum = %f \n", shared_data.sum);
delete shared_data.A, shared_data.B;
cout << "for n=" << N_THREADS*BLOCK_LEN<< " elements took " << t1 << " ms\n";
…
}
Finally set up the main function to create the threads and join them.

## Slide 17: HDL Solution ??
You would need to use fixed point arithmetic or floating point module
Need to create a state machine (unless you want all the elements to be multiplied at once and then added, see below) and memory blocks to store the vectors.
State machine solution will need a few
Clocks to cycle through the elements,
doing multiply and add for n clocks.

## Slide 18: System Verilog scalarproduct (experimental)
module scalarprod
#( parameter bits = 16, parameter N = 4 )
(
output [bits-1:0] result,
input [bits-1:0] A[0:N-1],
input [bits-1:0] B[0:N-1],
input clk,
input reset
);
reg [7:0]k; // Index counter
reg done; // Signals sum is complete
// Set result to 0 if in reset or accumulate products
always @(posedge clk)
if (reset) begin
k <= 7'd0;
done <= 1'd0;
result <= 0;
end else if(!done) begin
result <= result + A[k]*B[k];
k <= k + 1'b1;
done <= (k == N);
end
endmodule
Reset?
result=result+(A*B);
k= k + 1;
done = (k == N);
N
Y
N
done?
on clk
Y
end
k=0
done=0
result=0

## Slide 19: Parallel Programming Models
EEE4084F

## Slide 20: L05 - Linked Reading
Structures for parallel processing
D. Aspinall Pub date: 1990
Parallel processing is employed to achieve high performance by replication or a unique function by interconnecting diﬀerent processes. In each case the engineering problem, of providing the structure to interconnect the processors, is a combination of issues concerning not only the implementation technology but also the needs of the application. The concepts of geometric parallelism and algorithmic parallelism are introduced along with the concepts of granularity and degree of parallelism. The author discusses parallel processing paradigms and performance metrics such as latency, response crisis time and stimulus crisis time. The author discusses multi-computer systems; interconnection pathway, geometric parallelism by shared pathways, stars, rings and other topologies and the implementation of algorithmic parallelism. Parallelism within the mainframe computer is discussed. The von Neuman machine (processor-memory pair), eﬀect of a technology performance ratio; parallelism in the processor, pipelined computers and array computers.
File: L05 - 00084372 - Structures for parallel processing.pdf
Aspinall, D. "Structures for parallel processing." Computing & Control Engineering Journal 1.1 (1990): 15-22. DOI: 10.1049/cce:19900005
This paper, which is of a later date than Flynn’s work, presents additional parallel processing models, particularly ones that are not fully accurately for by Flynn’s taxonomy.

## Slide 21: Aspinall: structures of parallel processing
Parallel processing (author’s description):
  systems which allow more than one particular process to be active at any given instant.
Geometric Parallelism (SIMD*):
  all data are available at once and each node operates on a unique portion of it according to the same program of instructions
Algorithmic Parallelism:
  pattern of linkages by which the elements communicate with each other. Information flows from element to element in sequence to provide a result.
= processing node
= processing node
* This acronym will be encountered in next lecture

## Slide 22: Aspinall: structures of parallel processing
3x dimensions for the spaces of parallel processing…
  Process level: e.g. register transfer logic, instruction procedure or program.
  Granularity: ratio of the amount of computation (processing instructions per datum) to the to the amount of communication (transfer cost per datum). i.e. instructions : communications or result 1:N  fine grained (high interdependence, each result needs a lot of communication, much of the data) 1:1  medium grained e.g. sum(X) N:1  course grained (low interdependence, each computation needs little or no other data) e.g. X[1:10]=0
  Degree of Parallelism: (or DOP) how many operations can be simultaneously executed by a computer. (Useful for predicting potential performance of parallel programs).
f()
instruction
regs
f1
f2
f3
data

## Slide 23: Parallel System Approaches
Loaded & run when needed, time-shared system (very basic approach)
Communication by shared memory
Transputer paradigm: communicating by message passing – nowadays more commonly referred to as Message Passing (MP) model
Pipelined: stages of processing that runs in lockstep. Intermediate accumulator registers (result registers between stages) equals the degree of parallelism. Maximum parallelism achieved when stages fully synchronisation (i.e. no stalls).
Array/grid computers: mesh structure, neighbouring nodes share data
(from Aspinall, 1990)

## Slide 24: Parallel Programming Models
Parallel Programming Models:
  Data parallelism vs. Task parallelism
  Explicit parallelism / Implicit parallelism
  Shared memory / Distributed memory
Other parallel programming paradigms
  Object-oriented
  Functional and logic

## Slide 25: Data parallelism
Data-parallel =
  Parallel programs that emphasize concurrent execution of the same task on different data elements
Most programs for scalable parallel computers are data parallel in nature

## Slide 26: Task Parallel
Task parallel =
  Parallel programs that emphasize the concurrent execution of different tasks on the same or different data
Uses: Modularity reasons
Parallel programs, structured as a task-parallel composition of data-parallel components is common.

## Slide 27: Data vs. Task Parallel Examples
Data parallelism
Task Parallelism

## Slide 28: General Parallel Programming Models
Explicit Parallelism
  The programmer specifies directly the activities of the multiple concurrent threads of control that forms the parallel computation.
  Provides the programmer with more control over program behaviour and hence can be used to achieve higher performance.
Implicit Parallelism
  The programmer provides high-level specification of program behaviour.
  The compiler/library/framework needs to provide the means to implement the parallelism correctly and efficiently.

## Slide 29: Parallel Programming Tools
Parallel Virtual Machine (PVM)
  Distributed memory, explicit parallelism
PThreads
  Shared memory, explicit parallelism
Message-Passing Interface (MPI)
  Distributed memory, explicit parallelism
OpenMP
  Shared memory, explicit parallelism
Parallelizing Compilers
  Implicit parallelism

## Slide 30: Parallelizing Compilers
Automatically transform a sequential program into a parallel program.
Finds loops whose iterations can be executed in parallel.
Identifies data dependencies and orders the execution accordingly
Often done in stages.

## Slide 31: Types of Data Dependences
Flow dependence – Read-After-Write (RAW).
A true dependence as read a value after it has been written into a variable.
Anti-dependence - Write-After-Read (WAR). Writes new value into a variable after the old value has been read.
Output dependence - Write-After-Write (WAW). Write a new value into a variable and then later write another value into the same variable.
Data Dependences: used to determine what loops can or cannot be run in parallel.

## Slide 32: Example – data dependencies
line 1: A = 90;
line 2: B = A;
line 3: C = A + D
line 4: A = 5;
Flow dependence on A from line 1 to 2, and from 1 to 3. …
Dependencies ….
Anti dependence on A from line 2 to 4 and from line 3 to 4. …
Output dependence on A between line 1 and stmt 4.

## Slide 33: Example 1
line 1: for i = 1 to 1000
line 2: A(i) = B(i) + C(i)
line 3: D(i) = A(i)
line 4: next
Can this code be parallelized?
YES: There is a flow dependence on A(i) from line 1 to 2 in an iteration, but no dependences between any iterations.
Each iteration reads and writes to a different location in the array A, thus this loop can be executed in parallel – and even better we could execute the loop iterations in any order (so if some take longer to run than others that is OK).
A parallelizing compiler would split the 1000 iterations among the number of cores available
answer:

## Slide 34: Example 2
line 1: for i = 1 to 1000
line 2: A(i) = B(i) + C(i)
line 3: D(i) = A(i+1)
line 4: next
Can this code be parallelized?
YES – if you have a good compiler: This example clearly contains an anti-dependence from line 2 to 1…
But in the subsequent iteration a WRITE will be done after we have already READ it in the previous iteration.
Line 2 is meant to read an old value of A(i+1) before the same location will be written over in the next loop iteration.
If the iterations were spread among e.g. 4 threads, then thread #2 could have already written a new value to A(251) in its first loop iteration, long before thread #1 tries to read (the old value) in its last loop, iteration 250.
So the compiler could chicken out and say it is not parallelizable – or it could realize that this problem only occurs at the boundaries and attempt to modify the loop to solve the problem, e.g. using saving the last A(i+1) in temp variable.
answer:

## Slide 35: Shared Memory Models
EEE4084F
happy memories

## Slide 36: Shared Memory Model
Tasks share a common address space, can read and write to memory asynchronously.
Memory control access is needed (e.g., to cater for data dependencies), such as:
  Locks and semaphores to control access to shared memory.
In this model, the notion of tasks ‘owning’ data is lacking, so there is no need to specify explicitly the communication of data between tasks.

## Slide 37: Shared Memory Model: pros and cons
Adv: often allows program development to be simplified (e.g. compared to message passing, discussed in a later lecture).
Adv: Keeping data local to processor working on it conserves memory accesses (reducing cache refreshes, bus traffic and the like that occurs when multiple processors use the same data).
Disad: tends to become more difficult to understand and manage data locality, which may detract from the overall system performance.

## Slide 38: Using a Mutex
A mutex provides a means to protect parts of code so that only one thread runs that piece of code at a time
The mutex operations are
  lock : enter the protected code
  unlock : exit protected code / release key
#include <pthread.h>
// this is the library usually used
// instantiate a mutex:
pthread_mutex_t mutex;
C code snippets for using a mutex
// initialize the mutex
pthread_mutex_init(&mutex, NULL);
// lock the mutex
pthread_mutex_lock(&mutex);
// unlock the mutex
pthread_mutex_unlock(&mutex);
See example code at: http://apiexamples.com/c/pthread/pthread_mutex_lock.html
using mutexes so that neighbours are forced to talk (an adapted dining philosophers problem)

## Slide 39
Using scalar product pthreads type implementation for scenarios…
Introducing to some important terms related to shared memory

## Slide 40: Partitioned memory
[a1 a2 a1 a2 … am-1]
[b1 b2 b1 b2 … bm-1]
Thread 1
sum1
Vectors in
global / shared
memory
[am am+1 am+2 … an]
[bm bm+1 bm+2 … bn]
Thread 2
sum2
starts
main()
sum = sum1+sum2
Assuming a 2-core machine
1
1
2
2
a
b
main()
Memory access by thread

## Slide 41: Interlaced* memory
[a1 a3 a5 a7 … an-2]
[b1 b3 b5 b7 … bn-2]
Thread 1
sum1
Vectors in
global / shared
memory
[a2 a4 a6 … an-1]
[b2 b4 b6 … bn-1]
Thread 2
sum2
starts
main()
sum = sum1+sum2
Assuming a 2 core machine
a
b
* Data striping, interleaving and interlacing usually means the same thing.
main()
Memory access by thread

## Slide 42: Memory Partitioning Terms
Contiguous
Partitioned (or separated or split)
Interleaved/interlaced (or alternating or data striping)
Interleaved – large strides (e.g. row of image pixels at a time)
Interleaved – small stride (e.g. one word stride)
(the ‘stride’ in data interleaving or data striping refers to the size of the blocks alternated, generally
this is fixed but could be changeable, e.g. the last stride might be smaller to avoid padding data.)

## Slide 43
Image sources:
Stop watch slides 1 & 14, Gold bar: Wikipedia (open commons)
books clipart: http://www.clker.com (open commons)
Disclaimers and copyright/licensing details
I have tried to follow the correct practices concerning copyright and licensing of material, particularly image sources that have been used in this presentation. I have put much effort into trying to make this material open access so that it can be of benefit to others in their teaching and learning practice. Any mistakes or omissions with regards to these issues I will correct when notified. To the best of my understanding the material in these slides can be shared according to the Creative Commons “Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)” license, and that is why I selected that license to apply to this presentation (it’s not because I particulate want my slides referenced but more to acknowledge the sources and generosity of others who have provided free material such as the images I have used).