## Slide 1
Lecture 18 X:
HDL & VHDL Quick Recap
Lecturer:
Simon Winberg
Digital Systems
EEE4084F
Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)

## Slide 2: Outline for today
HDL & VHDL Recap

## Slide 3: YODA Project
Reminder about forming your teams
HDL coding for YODA, can use either of these or a combination of them:
  VHDL
  Verilog
  Schematic editor
Can also integrate with software that runs on the host PC, e.g. could have a C program that communicates with the FPGA

## Slide 4: HDL & VHDL Recap
EEE4084F

## Slide 5: Why use a Hardware Description Language (HDL)?
Rapidly model and test a functional system/subsystem
Means of modeling, testing, refining requirements and specification for a system
Formal verification (and an ‘interface’ to such mechanisms)
Testing designs options through use of simulation
Synthesis of ICs / digital logic systems
General benefits of the HDL approach:
Towards better and more reliable designs
Avoid design errors
Reduce costs and time
Major reasons for using a HDL:

## Slide 6: Summary of Elements of the VHDL Paradigm
Entity : A part of the system (can be a subsystem)
Ports : Connections (or interfaces) between
Behavior : What an entity does
Structure : What an entity comprises
Analysis : Checks syntax, etc. Does various automated tests and simulations on the design to verify that it can be synthesized and deployed on a particular programmable device / IC.
Test Bench : How entities or a whole design is tested
Synthesis : Deciding gates and how to connect them / generating the bitstream to configure the hardware.

## Slide 7: PLD/FPGA Development Flow
Synthesis
- Translate Design into Device Specific Primitives
- Optimization to Meet Required Area & Performance Constraints
Place and Route (PAR)
- Map primitives to specific locations inside FPGA with reference to area & performance constraints
- Specify routing resources to use
Design and RTL Coding
- Behavioral or Structural Description of Design - Writing VHDL, deciding i/o, formulating tests
RTL Simulation
- Functional Simulation
- Verify Logic Model & Data Flow
- View model-specified timing
LE
M512
M4K
I/O
Design Specification
This development cycle diagram is an adaptation of that prepared by Dr. Junaid Ahmed Zubairi,
Avail: http://www.cs.fredonia.edu/zubairi/training/fpga.ppt
… PTO …

## Slide 8: Development Flow
Timing Analysis
- Verify performance specifications
- Static timing analysis
Gate Level Simulation
- Timing simulation
- Verify design will work on target platform
Program and test on hardware
- Generate bit file - Program target device
- Activate the system
tclk
Place and Route (PAR)

## Slide 9: Development Flow: Where is most time spent?
Design and RTL Coding
- Behavioral or Structural Description of Design - Writing VHDL, deciding i/o, formulating tests
Every development project is different. In my own experience, most of the time is probably spent…
Engineer’s time
Timing Analysis
- Verify performance specifications
- Static timing analysis
tclk
PC’s time
Eish!
Eish!
Place and Route (PAR)
- Map primitives inside FPGA
- Specify routing resources to use

## Slide 10: VHDL Basics
VHSIC = Very-High-Speed Integrated Circuit
VHDL = Very High-level Description Language
VHDL = Very Hard Development Language
(although you would be kind of right to say VHDL has these properties)
*
+
*
+
What VHDL stands for….
VHDL = VHSIC Hardware Description Language

## Slide 11: VHDL Terms and Keywords
Entity: designs are expressed in terms of entities, these are components that are interfaced together via ports and maps
Architecture: Describes the behaviours of the entity. Each entity can have multiple architectures.
Configuration: binds a component instance to a entity-architecture pair
Entity (black box)
Ports
Architecture
 Configuration 
Source: Perry, D. 2002. VHDL Programming by Example. 4th ed. McDraw-Hill.

## Slide 12: Important Terms
Top-level module: module at the top of the hierarchy
Package: collection of commonly used data types, subroutines, for implementing architectures
Driver: source on a signal
Bus: a signal that can have its sources turned off
Signal vector: what we usually think of as a bus
Attribute: data attached to VHDL objects (e.g., event status)
Generic: a parameter to pass information to an entity
Process: a basic unit of execution. Multiple processes are usually active at a time.
Source: Perry, D. 2002. VHDL Programming by Example. 4th ed. McDraw-Hill.

## Slide 13: VHDL Example
Let’s implement this combinational logic circuit:
A
B
C
AND2
1-bit inputs
1-bit output
AND2 operation: C = A AND B

## Slide 14: VHDL Example
Start by defining the entity:
-- Here’s a comment
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity AND2 is
port ( A : in STD_LOGIC;
B : in STD_LOGIC;
C : out STD_LOGIC );
end AND2;

## Slide 15: VHDL Example
Then add an architecture:
…
architecture AND2bhv of AND2 is
begin
C <= A and B; -- The <= links signals and ports
end AND2bhv;
As is the program should compile in Xilinx ISE; the system will create an instance of AND2 as it is the top level module, so no need to add an explicit configuration statement.
Name of this architecture
Name of architecture

## Slide 16: Concurrent operation
Each statement in a VHDL architecture block executes concurrently, whenever there is a change / event
e.g.
  C <= A and B; -- executes when A or B changes
  D <= A or B; -- executes when A or B changes
If A were to change (e.g. A changes from 0 to 1) then both the lines will execute at once)

## Slide 17: Sequential operation
library ieee; use ieee.std_logic_1164.all;
entity fulladder is
port (A1, A2, Cin: in std_logic;
sum, Cout : out std_logic );
end fulladder;
architecture arch1 of fulladder is
begin
process(A1,A2,Cin) -- define a sequential operation
begin
sum <= Cin xor A1 xor A2;
Cout <= (A1 and A2) or (Cin and (A1 xor A2));
end process;
end arch1;
This line runs first
Then this line runs
Note: two process blocks in the same architecture block run concurrently
Sequential operation is described within a PROCESS block. Example:
Sensitivity list (note not sensitive to Cout)
A process doesn't have a name so you have to say ‘end process’
General rule for end: if the structure has a name say ‘end name’, if it doesn’t ‘use structure_keyword’.

## Slide 18: VHDL coding
Outside a PROCESS:
COMPONENT declaration
SELECT statement
WHEN – conditional assignment
Inside a PROCESS:
IF-THEN-ELSE
CASE statement
Best way to learn VHDL is to practice coding with it.
See the VHDL Cheat Sheet on VULA
General thing to remember to get the syntax right:
But if you haven’t done VHDL then note…

## Slide 19: VHDL coding
Note that: we will dive into Verilog to prepare you for Prac4.
So if you haven’t done VHDL, might as well focus on Verilog.
But take note:
Computer engineers often end up having to manage with both flavors of HDL to save time by reusing designs.
The YODA project can be done in either VHDL, Verilog or a combination of the two.
Many large projects end up being a combination of the two just because: engineers might not know the other, or the one HDL might be better suited to solving a problem than the other.
?

## Slide 20: Recommended Steps for VHDL coding
Plan dataflow and code entities
Implement behaviours
Structural modelling (build complex entities using lower level ones)
Recommended online VHDL support:
http://esd.cs.ucr.edu/labs/tutorial/
This site provides a collection of useful VHDL example code and tutorials

## Slide 21: Next lecture
Verilog coding

## Slide 22
Image sources:
PLD illustration on title slide - Wikipedia Open Commons
FPGA chip illustrations - Wikipedia Open Commons
Stuck in Mud – fickr (CC2 for free reuse and modification)
Typing ninja – Pixabay http://pixabay.com/ (public domain)
Disclaimers and copyright/licensing details
I have tried to follow the correct practices concerning copyright and licensing of material, particularly image sources that have been used in this presentation. I have put much effort into trying to make this material open access so that it can be of benefit to others in their teaching and learning practice. Any mistakes or omissions with regards to these issues I will correct when notified. To the best of my understanding the material in these slides can be shared according to the Creative Commons “Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)” license, and that is why I selected that license to apply to this presentation (it’s not because I particulate want my slides referenced but more to acknowledge the sources and generosity of others who have provided free material such as the images I have used).