## Slide 1
Lecturer:
Simon Winberg
Digital Systems
EEE4084F
Lecture 24X
RC Platform Case Studies 2/2:
Large & small FPGA-based RC systems
Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)
Microprocessor-based: The Cell Broadband Engine Architecture, IBM Blade
FPGA-based:
PAM, VCC, SPLASH …
(this lecture)
(previous lecture)
NOT IN 2018 EXAM

## Slide 2: Lecture Overview
Large-scale FPGA-based RC system examples
  PAM, VCC, Splash
Small-scale FPGA-based RC system examples
  PRISM
  Algotronix CAL, XC620,
  Cray Research XD1,
  SRC
  Silicon Graphics RASP

## Slide 3: Large-scale RC Systems
A look at platforms architectures

## Slide 4: Large RC System - PAM
Programmable Active Memories (PAM)
  Produced by Digital Equipment Corp (DEC)
  Used Xilinx XC3000 FPGAs
  Independent banks of fast static RAM
Host
CPU
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
DRAM
Digital Equipment Corp. PAM system (1980s)
Image adapted from Hauck and Dehon (2008) Ch3

## Slide 5: Large RC System - VCC
Virtual Computer Corporation (VCC)
First commercially commercial RC platform*
Checkerboard layout of
  Xilinx XC4010 devices and
  I-Cube programmable interconnection devices
  SRAM modules on the edges
* Hauck and Dehon (2008)
…
…
…
…
…
…
…
…
…
…
…
VCC Virtual Computer
FPGA
SRAM
SRAM
FPGA
FPGA
SRAM
I-Cube
FPGA
FPGA
FPGA
I-Cube
FPGA
I-Cube
I-Cube
FPGA
SRAM
SRAM
FPGA
FPGA
FPGA
I-Cube
I-Cube
FPGA
SRAM

## Slide 6: Large RC System - Splash
Summary of the Splash system
Developed initially to solve the problem of mapping the human genome and other similar problems. Design follows a reconfigurable linear logic array. The SPLASH aimed to give a Sun computer better than supercomputer performance for a certain types of problems. At the time, the performance of SPLASH was shown to outperform a Cray 2 by a factor of 325. FPGAs were used to build SPLASH, a cross between a specialized hardware board but more flexible like a supercomputer. The SPLASH system consists of software and hardware which plugs into two slots of a Sun workstation. **
* Hauck and Dehon (2008)
SRC Splash version 2
Dedicated
controller
…
…
…
…
SRAM
FPGA
FPGA
SRAM
FPGA
SRAM
FPGA
SRAM
FPGA
SRAM
FPGA
SRAM
FPGA
SRAM
Crossbar
Dev. by Super Computer Research (SCR) Center ~1990
Well utilized (compared to previous systems).
Comprised linear array of FPGAs each with own SRAM *
**Adapted from: Waugh, T.C., "Field programmable gate array key to reconfigurable array outperforming supercomputers," Custom Integrated Circuits Conference, 1991., Proceedings of the IEEE 1991 , vol., no., pp.6.6/1,6.6/4, 12-15 May 1991 doi: 10.1109/CICC.1991.164051
Illustration of the
SPLASH design
(adapted from *)

## Slide 7: Small-scale RC Systems
A look at platforms architectures

## Slide 8: Small RC Systems
Brown University’s PRISM
  Single FPGA co-processor in each computer in a cluster
  Main CPUs offloading parallelized functions to FPGA
Algotronix
  Configurable Array Logic (CAL) – FPGA featuring very simple logic cells (compared to other FPGAs)
  Later become XC6200 (when CAL bought by Xilinx)
* Hauck and Dehon (2008)

## Slide 9: Reconfigurable Supercomputers
Cray Research
  XD1: 12 processing nodes
  6x ADM Opteron processors
  6x Reconfigurable nodes built from Xilinx Vertex 4
  Each XD1 in own chassis, can connect up to 12 chassis in a cabined (i.e. 144 processing nodes)
SRC
  Traditional processor + reconfig. processing unit
  Based on Xilinx Virtex FPGAs
Silicon Graphics
  RASP (reconfigurable application-specific processor)
  Blade-type approach of smaller boards plugging into larger ones
Ref: Hauck and Dehon Ch3 (2008)

## Slide 10: Additional Reading
Reading
  Reconfigurable Computing: A Survey of Systems and Software (ACM Survey) *
* Compton & Hauck (2002) .“Reconfigurable Computing: A Survey of Systems and Software” In ACM Computing Surveys, Vol. 34, No. 2, June 2002, pp. 171–210.
  (not specifically examined, but can help you develop insights that help you demonstrate a deeper understanding to problems)
-- End of the Cell Processor case study --

## Slide 11: Conclusion & Plans
Reading
  Hauck, Scott (1998). “The Roles of FPGAs in Reprogrammable Systems” In Proceedings of the IEEE. 86(4) pp. 615-639.
Next lecture:
  Amdahl’s Law
  Discussion of YODA phase 1

## Slide 12
Image sources:
Wikipedia open commons
Disclaimers and copyright/licensing details
I have tried to follow the correct practices concerning copyright and licensing of material, particularly image sources that have been used in this presentation. I have put much effort into trying to make this material open access so that it can be of benefit to others in their teaching and learning practice. Any mistakes or omissions with regards to these issues I will correct when notified. To the best of my understanding the material in these slides can be shared according to the Creative Commons “Attribution-ShareAlike 4.0 International (CC BY-SA 4.0)” license, and that is why I selected that license to apply to this presentation (it’s not because I particulate want my slides referenced but more to acknowledge the sources and generosity of others who have provided free material such as the images I have used).